THE WEST COAST REGIONAL COUNCIL

NELSON CREEK RATING DISTRICT

ASSET MANAGEMENT PLAN

October 2014

CONTENTS

EXECUTIVE SUMMARY	3

SECTION 2: SERVICE LEVELS	6

SECTION 3: FUNDING	8

SECTION 4: PERFORMANCE MEASURES	9

APPENDIX 1:  WORKS EXPENDITURE SINCE 1988	10

APPENDIX II:  ASSET REGISTER AND INFRASTRUCURE MAPS	11

## EXECUTIVE SUMMARY

Under the Local Government  Act 2002 Councils are required to develop ‘Asset Management Plans’ to demonstrate that they are managing the infrastructure for which they have responsibility.

This plan sets out the history of the scheme so there is a record of the major decisions, including expenditure. It identifies the Objective(s) of the scheme as well as the methods of monitoring the condition of the assets, and determining the annual maintenance needed to retain the service level.

The Nelson Creek Rating District extends 2.3 kilometres upstream of the State Highway Bridge and downstream for 1.1 kilometres to the Rail Bridge. The area protected is predominantly used for dry stock grazing and commercial use. Community infrastructure such as roads, power and telephone lines all derive benefit from the river control system.

The Infrastructural Asset Register details all of the Scheme’s assets and their latest valuation.

External Contributions

Both NZ Transport Agency (ex Transit New Zealand) and OnTrack NZ (ex Tranz Rail) make contributions at a fixed percentage rate to the annual maintenance of the Nelson Creek scheme. NZTA pays 35% of maintenance costs above the State Highway Bridge and OnTrack pays 50% of any maintenance works between the rail and road bridges.

1.1	PURPOSE OF AN ASSET MANAGEMENT PLAN

This Asset Management Plan defines the objectives of the Nelson Creek Rating District scheme for which the Regional Council has the maintenance responsibility. It also provides a basis upon which the effectiveness of maintenance performance can be measured.

The asset management plan:

- Identifies the service level for the Rating District.

- Describes the history of the rating district and identifies it’s assets.

- Describes the methods used to maintain the service level of these assets.

- Complies with the regulatory requirements of the Local Government Act 2002.

# 1.2	BACKGROUND

Prior to 1945 the Lower Nelson Creek area upstream of the State Highway Bridge had been prone to severe floods and erosion, causing problems of inundation of farmland and the closure of 1 kilometre of State Highway 7.  Individual landowners had carried out simple and cheap forms of river protection works.  Old dredge screens and galvanised iron tanks filled with stones were used to form spur groynes to protect land from erosion.

On 18 May 1945 the Westland Catchment Board held its first meeting. The importance of this date is significant in that direct access to central government resources through the Soil Conservation and Rivers Control Council were made available for river protection works.

Flooding and erosion between the old Road Bridge and the downstream new State Highway Bridge continued until 1961. Minimal works in the form of tree, rope and drum groynes with some rock groynes were carried out in an attempt to halt the erosion and flooding processes.

On 18 December 1961 the Ministry of Works requested the Westland Catchment Board to prepare an estimate of river training works to alleviate flooding of State Highway 7 at Nelson Creek.  An investigation of a river control scheme over a length of 1.2 kilometres between Drennan’s Bridge and the State Highway Bridge was undertaken.  Minor channel reconstruction works were carried out during this period.

On 29 March 1963 a serious flood occurred, crossing the main highway from the bridge to the hill on the north side of the valley. On 3 May 1966 work worth $7,700 was approved and work commenced on the construction of permeable groynes, channel work, and the driving of rails and placement of heavy wire rope over a distance of 760 metres. Work had been in progress for 4 months, when on the 8 November 1963 a flood again overtopped the stopbank, flooded 3 properties and blocked the State Highway.

Between 1963 and 1973 a considerable amount of work was carried out, mainly in the form of channel clearing with some additional rockwork in the form of spur groynes.  Between 1973 and 1978 rock was used more extensively to increase stability along both banks.

In April 1978 floodwater breached a stopbank on the right bank 400 metres downstream of the old Drennan’s bridge and again inundated farmland and the State Highway.

The Ministry of Works again sought costs of a comprehensive river control scheme.  In 1980 the existing stopbank was raised by 1 metre over a length of 240 lineal metres.  Also in January 1980 New Zealand Railways sought advice on remedial action required to alleviate erosion problems at the rail bridge.  In October 1980 New Zealand Railways carried out its own protection works, 13,000 tonnes of rock being utilised to protect the rail embankment.

On 18 February 1981 the Westland Catchment Board presented a proposal to protection land on the right bank, above the State Highway Bridge.  The design was based on protecting the land from a 50 year return flood. The works involved construction of a stopbank 1.8m high from the State Highway Bridge upstream for 1.6 kilometres and the placement of 1,000 tonnes of rock.

On 5 March 1982 National Roads Board approved 50% funding as its share of the proposed works.

On 8 September 1983 a revised estimate, due to floods on 9 and 10 July 1983, was put forward to those involved. The revised estimate was accepted which involved 21,400m3 of fill and 1,200 tonnes of rock at a total cost of $56,000. The contract was let to H. Langridge and Sons on 25 November 1983.

On 23 July 1984 a classification covering all works on Nelson Creek between the old Grey County Bridge and the Tranz Rail Bridge. The proposed left bank costs totalled $31,000 (NZR Share 50%) and the right bank costs totalled $32,500 (NZR Share 50%).

The proposal gained New Zealand Railway’s approval on 10 December 1984.

At a ratepayers meeting on 22 July 1985 it was agreed to extend the Rating District Classification to include all works downstream to the rail bridge. The classification would be based on Land Value. This classification was adopted by the Westland Catchment Board on 26 May 1986. This was later changed to Land Area basis on 20 April 1993.

In the period 1996 to 2001 several ratepayers expressed concern at apparent anomalies at residential rating within the Mill site (Savage’s property).

A request was made to carry out a reclassification at the rating District’s Annual General Meeting on 3 April 2001.

A revised differential, land area based rating district was prepared and was approved by Special Order, by the West Coast Regional Council on 9 July 2002.

1.3 	DESCRIPTION OF ASSETS

The Rating District assets consist of all those works outlined in the Infrastructural Asset Register. The total replacement value of these works was $2.3M as at June 2014.

The rateable capital value of land and buildings within the confines of the scheme is $12,293,000 but this figure does not take into account the value of road and rail infrastructure that is being protected.

1.4	MAINTENANCE EXPENDITURE

Appendix I shows expenditure since 1988. The average annual expenditure is $15,776

## SECTION 2: SERVICE LEVELS

2.1	OBJECTIVES

The objective of the Nelson Creek Rating District is to reduce bank erosion and flooding along the Upper and Lower reaches of the Nelson Creek.

There have been a mix of design standards during the life of this scheme. The original stopbanks were built to 900mm above the highest known flood. After 1983, sections of stopbank were built to contain a flood of 539 cumecs which at that time was estimated to be a 1 in 50 year return period flood. However, no recent flood flow analysis has been undertaken for this river therefore the current level of protection given by the stopbanks is unclear and any service level that has been identified in the past should be treated with caution.

The Council has suggested that an analysis be commissioned to quantify the actual level of protection that the scheme currently provides. The rating district has not yet decided if they wish to have any new flood analysis under taken. Given that there has been no analysis carried out the scheme structures will continue to be maintained to the dimensions that they were originally constructed.

2.2	MAINTENANCE PROGRAMME

An annual maintenance programme will be prepared each year in consultation with the ratepayers, prior to adoption by the Council for inclusion in the Annual Plan.

In preparing the annual maintenance programme consideration will be given to:

- an inspection to identify works requiring immediate repair.

- works anticipated as being required given a ‘normal’ season.

- flexibility to meet unbudgeted damages.

Stopbanks

Stopbanks are man made structures generally running parallel to the flow of the river that are built to raise the bank level and hence increase the capacity of the river. They are usually constructed of compacted river gravels with a grass cover and do not have the strength to resist the erosive forces of a river in flood without adequate bank protection works in place.

Maintenance includes repair of any scouring, vegetation removal to facilitate access, control of stock to prevent damage to stopbank batter slopes, topping up of stopbanks as required to maintain stopbank capacity in terms of design.

Stopbanks can potentially be damaged by:

- Failure of a training groyne such as a rock retard which can allow the full force of the river to suddenly run along a relatively unprotected stopbank, and cause scouring of stopbanks in excess of 50 metres in length

- Overtopping: Stopbanks are generally not designed to sustain overtopping. They may however be capable of sustaining minor overtopping for a short duration in flows not exceeding 100mm in depth over the top of the bank. Overtopping of durations greater than an hour may scour the back batter resulting in failure of the structure, it is therefore important to ensure there is an even and strong vegetation cover on the landward batter.

- Piping: Flow through porous bank or foundation material can wash out fines leading to a collapse.

- Stock and Vehicles: Can remove cover and wear ruts in surface causing weakness.

- Construction: Construction of pipelines cables under stopbanks as well as holes on top of stopbanks can weaken the structure. Drainage channels should not be located at the toe of stopbanks.

- Earthquake: Stopbanks can be cracked by vertical or horizontal displacement, or by liquefaction of the foundation material.

Erosion Control / River Training

Erosion control works consist of rock placed in continuous riprap, spur groynes, stub groynes, strongheads, hook groynes, and in river training retards. 	Erosion control and river training structures are built to provide protection to stopbanks and natural bush from the rivers erosive forces during floods by training the river into a stable pattern or reduce velocities along stopbanks using stub rock groynes.

Only limited river training is carried out by way of channel improvements by diversion or extraction of river gravels. This is generally accepted as only having a limited and temporary influence on the channel hydraulics (performance).

Erosion control structures are constructed to absorb the energy of the river, to control the alignment of the flow of the rivers, and subsequently give the required protection to stopbanks and natural banks. Because of this they are the areas with the major exposure to damage. 	The meander of a river can change significantly by floods of only moderate duration.  This can result in an acute angle of attack of protection structures resulting in damage which is disproportional to the flood discharge. Likewise erosion control works already weakened from previous floods may sustain damage disproportionate to the flood discharge.

Repairs to bank protection structures must be undertaken swiftly to ensure:

- Rock training walls are kept to the required height to lessen failure.

- Any slumping of rock off strongpoints, spur groynes and rip rap are topped up.

- Rock is of a durable nature, angular and of the correct grading size.

2.3	DAMAGE EXPOSURE

River control works are constructed in a very high energy environment with the purpose of resisting and absorbing some of that energy.  It is considered that no matter what the standard of maintenance carried, it is inevitable that damage will occur to structures.

An assessment of maximum damage potential was derived from estimating the damage ratios and costs for three flood events and is in vicinity of $400,000.

| FLOOD EVENT SIZE | VALUE | DAMAGE RATIO | DAMAGE EXPOSURE |
| --- | --- | --- | --- |
| 20 Year | $2,306,144 | 10% | $230,61 |
| 100 Year | $2,306,144 | 20% | $461,228 |
| 500 Year | $2,306,144 | 25% | $576,536 |

## SECTION 3: FUNDING

3.1	MAINTENANCE

Maintenance is funded by targeted rates, the level of rating being determined each year in the Annual Plan process following:

- Preparation of an annual works programme and corresponding budget.

- Consultation with Rating District.

- Adoption of draft programme and budget by Council.

- Adoption of final Annual Plan by Council.

3.2	DAMAGE REPAIRS

Routine damage repairs are funded by a combination of:

- carrying out work as scheduled in annual works programme.

- reprioritising works identified in the annual works programme.

- use of financial reserves.

Major damage repairs would be funded by loans raised by the Council and repaid by targeted rating over a number of years.

3.3	FINANCIAL RESERVES

Financial reserves are held within each rating districts account to provide the following.

- meet the costs of unscheduled works.

- enable an immediate response to flood damage repairs.

- prevent major fluctuation in rating levels annually.

The level of financial reserves held in each rating account is determined by the assessment of risk damage and the need for unprogrammed works.

3.4	DEPRECIATION

Rating District schemes are designed to be maintained in perpetuity by constantly repairing and replacing component parts which are damaged by the constant wear and tear. Because there is a constant cycle of replacement of elements of the infrastructure, depreciation of the value of the assets is not appropriate and funding of depreciation is not necessary. This approach is consistent with the NZ Infrastructure Asset Valuation and Depreciation Guidelines (Section 5.4.4).

## SECTION 4: PERFORMANCE MEASURES

The overall performance measure is that the infrastructure assets are maintained to meet their service levels at all times.

The following procedures will be adopted to ensure the adequacy of maintenance.

Annually

- Produce annual works report for the rating district to include type of work to be undertaken, quantities, location and costs.

- Organise contracts for agreed scheme work, oversee contract completion and report to Council.

(iii)	Report on works undertaken during the previous financial period to the rating district ratepayers and Council.

Performance Measure

No reports of stopbanks or erosion protection works requiring repairs without an agreed programme of remedial work in progress.

Triennially

(i)	Re-fly aerial photographs of the area, analysing these photographs to assess changes in river meander patterns that could impact on Rating District Assets.

(ii)	Re-measure cross section river profiles to determine whether the riverbed is stable, or aggrading, and to identify management issues or options.

(iii)	Revaluation of the asset schedule to include any additional rock placed on stopbanks and bank protection works over the three year period.

(iv)	Review this Asset Management Plan

Performance Measure

Report to Council and ratepayers on revaluation of assets and the Plan review.

## APPENDIX 1:  WORKS EXPENDITURE SINCE 1988

| 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 7,042 | 29,516 | 16,905 | 16,460 | 7,975 | 11,707 | 21,577 | 12,629 |
| 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 |
| 5,534 | 35,831 | 22,832 | 23,863 | 16,741 | 678 | 3,307 | 156 |
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 |
| 1,413 | 10,774 | 33,184 | 16,197 | 1,957 | 33,227 | 19,528 | 42,676 |
| 2012 | 2013 | 2014 |  |  |  |  |  |
| 19,008 | 12,614 | 2,629 |  |  |  |  |  |

| Total Expenditure | $ 425,960 |
| --- | --- |
| Average Expenditure | $ 15,776 |
| Average Expenditure as a % of Asset Value | 0.68% |

As at 30 June 2014, the value of the Nelson Creek Rating District Scheme assets is $2,306,144

APPENDIX II – ASSET REGISTER AND INFRASTURE ASSET MAPS

| NELSON CREEK RATING DISTRICT |  |  |  |
| --- | --- | --- | --- |
| Infrastructural Assets - Amended to 30 June 2014 |  |  |  |
| Refer to Drawing No 914/363 Sheets 1 & 2 |  |  |  |
|  |  |  | Rock | Fill | Stockpile |
|  |  |  | Tonnes | m³ | Tonnes |
| A |  | RIGHT BANK - BETWEEN BRIDGES |  |  |  |
| 1 |  | Rock rip rap over 30 metres |  |  |  |
|  |  | 2.5m high, 4m deep, 2:1 batters | 600 |  |  |
|  |  | Added Nov 98 | 300 |  |  |
| 2 |  | 20 tonnes rock stockpile |  |  | 20 |
| 3 |  | Continuous rock rip rap |  |  |  |
|  |  | 4m deep, 2.5 metres high |  |  |  |
|  |  | 2:1 batters, 86 lineal metres | 1500 |  |  |
|  |  | Added December 2008 - Contract R 2008 / 13 | 100 |  |  |
| 4 |  | Continuous rock rip rap |  |  |  |
|  |  | 2 metres high, 2 metres deep |  |  |  |
|  |  | 2:1 batters, 20 metres lineal | 350 |  |  |
|  |  | Added May 2010 - Paul steegh Contract R 2010.9 | 200 |  |  |
| 4 | a | Stopbank, 110 lineal metres |  |  |  |
|  |  | 2.5m metres high (Average), |  |  |  |
|  |  | 2:1 batters, 5 metres topwidth |  | 2750 |  |
| 5 |  | Rock Spur | 10 |  |  |
| 6 |  | Rock Spur | 100 |  |  |
| 7 |  | Rock Spur | 50 |  |  |
| 8 |  | Rock Spur | 150 |  |  |
| 8 | a | Rock Spur | 150 |  |  |
|  |  | Added Nov 98 | 25 |  |  |
| 8 | b | Rock Spur | 150 |  |  |
|  |  | Added Nov 98 | 25 |  |  |
|  | c | Added Nov 98 | 25 |  |  |
|  | d | Added Nov 98 | 25 |  |  |
|  | e | Added Nov 98 | 25 |  |  |
| 9 |  | Rock Spur | 180 |  |  |
| 10 |  | Rock Spur | 150 |  |  |
| 11 |  | Rock Spur | 240 |  |  |
| 12 |  | Rock Spur | 120 |  |  |
| 12 | a | Rock rip rap | 170 |  |  |
| 13 |  | Rock Spur | 80 |  |  |
| 13 | a | Rock rip rap | 170 |  |  |
| 14 |  | Rock Spur | 130 |  |  |
| 15 |  | Rock spur | 100 |  |  |
| 15 | a | Rock rip rap | 100 |  |  |
| 16 |  | Rock spur | 100 |  |  |
|  |  | Added March 2006 | 100 |  |  |
| 17 |  | Rock spur | 100 |  |  |
| 18 |  | Rock spur | 80 |  |  |
| 19 |  | Rock spur | 100 |  |  |
| 20 |  | Rock spur | 100 |  |  |
| 21 |  | Rock spur | 100 |  |  |
| 22 |  | Rock spur | 20 |  |  |
|  |  | Added March 2006 | 100 |  |  |
| 23 |  | Rock spur | 100 |  |  |
| 24 |  | Rock spur | 100 |  |  |
| 25 |  | Rock spur | 140 |  |  |
| 26 |  | Rock spur | 50 |  |  |
| 27 |  | Rock spur | 50 |  |  |
| 28 |  | Rock spur | 150 |  |  |
| 28 | a | Rock rip rap | 150 |  |  |
| 29 |  | Rock spur | 100 |  |  |
| 30 |  | Rock spur | 100 |  |  |
| 30 | a | Rock rip rap (between spurs #30 & # 31) | 50 |  |  |
| 31 |  | Rock spur | 200 |  |  |
| 32 |  | Rock spur | 50 |  |  |
| 32 | a | Rock rip rap (between spurs #32 & # 33) | 30 |  |  |
| 33 |  | Rock spur | 50 |  |  |
| 34 |  | Rock spur | 50 |  |  |
| 35 |  | Rock spur | 50 |  |  |
| 36 |  | Rock spur | 50 |  |  |
| 38 |  | Rock rip rap, 2:1 batters |  |  |  |
|  |  | 30 lineal metres, 5 metres high |  |  |  |
|  |  | 2 metres deep | 850 |  |  |
| 39 |  | Stopbank (Point A to B) |  |  |  |
|  |  | 1070 lineal metres |  |  |  |
|  |  | 4 metre topwidth, 2:1 batters |  |  |  |
|  |  | 2.5 metre high (average) |  | 24100 |  |
| 135 |  | Rock rip rap | 260 |  |  |
|  |  | Added April 2002 | 60 |  |  |
|  |  | Added December 2008 Contract R 2008 / 13 | 300 |  |  |
| 154 |  | New Cut-off bank over 75 metres - November 2012 |  |  |  |
|  |  | MBD Contracting | 604 | 750 |  |
| B |  | LEFT BANK (BETWEEN BRIDGES) |  |  |  |
| 40 |  | Rock spur | 80 |  |  |
| 40 | a | Rock weir | 50 |  |  |
|  |  | Riprap Added September 2006 |  |  |  |
| 40 | b | Rock stockpile | 212 |  | 50 |
| 40 | c | Rock spur | 50 |  |  |
| 40 | d | Rock spur | 50 |  |  |
| 40 | e | Rock spur | 50 |  |  |
| 41 |  | Rock spur | 80 |  |  |
| 41 |  | Added Nov 98 | 50 |  |  |
| 41 | a | Added Nov 98 | 50 |  |  |
| 42 |  | Rock spur | 80 |  |  |
| 43 |  | Rock spur | 80 |  |  |
| 43 | a | Rock Spur |  |  |  |
|  |  | Added June 2006 | 22 |  |  |
| 44 |  | Rock spur | 80 |  |  |
| 44 | a | Added Nov 98 | 30 |  |  |
| 45 |  | Rock spur | 80 |  |  |
| 45 | a | Added Nov 98 | 50 |  |  |
| 46 |  | Rock spur | 80 |  |  |
| 46 | a |  | 30 |  |  |
| 47 |  | Rock spur | 80 |  |  |
| 47 | a | Added Nov 98 | 50 |  |  |
| 48 |  | Rock spur & riprap over 20 metres | 80 |  |  |
|  |  | Added May 2010 - Paul Steegh | 180 |  |  |
| 49 |  | Rock spur | 80 |  |  |
| 49 | a | Added Nov 98 | 220 |  |  |
| 50 |  | Rock spur | 80 |  |  |
| 50 |  | Added Nov 98 | 30 |  |  |
|  |  | Added November 2007 | 100 |  |  |
| 50 | a | Added Nov 98 | 47 |  |  |
| 51 |  | Rock spur | 100 |  |  |
| 52 |  | Rock spur | 50 |  |  |
| 53 |  | Rock spur | 50 |  |  |
| 54 |  | Rock spur | 50 |  |  |
| 55 |  | Rock spur | 50 |  |  |
| 56 |  | Rock spur | 50 |  |  |
| 57 |  | Rock spur | 50 |  |  |
| 58 |  | Rock spur | 50 |  |  |
| 59 |  | Rock spur | 50 |  |  |
| 60 |  | Rock spur | 50 |  |  |
| 61 |  | Rock spur | 50 |  |  |
| 62 |  | Rock spur | 50 |  |  |
| 63 |  | Rock spur | 50 |  |  |
| 64 |  | Rock spur | 80 |  |  |
| 65 |  | Rock spur | 50 |  |  |
| 66 |  | Rock spur | 50 |  |  |
| 67 |  | Rock spur | 50 |  |  |
| 68 |  | Rock spur | 50 |  |  |
| 69 |  | Rock spur | 50 |  |  |
| 69 | a | Added Nov 98 | 450 |  |  |
| 70 |  | Rock spur | 50 |  |  |
| 71 |  | Rock spur | 50 |  |  |
| 72 |  | Rock spur | 80 |  |  |
| 73 |  | Rock spur | 50 |  |  |
|  |  | Added June 2006 | 32 |  |  |
| 74 |  | Rock spur | 50 |  |  |
| 75 |  | Rock spur | 50 |  |  |
|  |  | Added June 2006 | 20 |  |  |
| 75 | a | Riprap Added November 2004 | 100 |  |  |
|  |  | Added March 2005 | 40 |  |  |
|  |  | Added March 2006 | 100 |  |  |
| 76 |  | Rock spur | 50 |  |  |
| 77 |  | Rock spur | 50 |  |  |
| 78 |  | Continuous rock work |  |  |  |
|  |  | 80 lineal metres |  |  |  |
|  |  | 4 metres high, 2 metres deep |  |  |  |
|  |  | 2:1 batters | 1500 |  |  |
|  |  | 4 new spurs added Aug 2010 R.2010.12 - Foster | 200 |  |  |
| 79 |  | Stopbank (Point C to D) |  |  |  |
|  |  | Average height 2.5 metres |  |  |  |
|  |  | 2:1 batters, 4 metres topwidth |  |  |  |
|  |  | (940 lineal metres) |  | 21150 |  |
|  |  | Added March 2006 | 150 |  |  |
| 79 | a | Rock riprap |  |  |  |
|  |  | Added March 2006 | 200 |  |  |
| 80 |  | Continuous rock rip rap |  |  |  |
|  |  | 30 lineal metres | 300 |  |  |
| C |  | RIGHT BANK ABOVE ROAD BRIDGE |  |  |  |
| 81 | a | Rock spur | 50 |  |  |
| 81 | b | Rock spur | 50 |  |  |
| 81 | c | Rock spur | 50 |  |  |
| 81 | d | Rock spur | 50 |  |  |
|  |  | Added June 2012 - G.H. Foster as riprap | 436 |  |  |
| 81 | e | Rock spur | 50 |  |  |
| 82 |  | Continous rock work 100 lineal metres | 1000 |  |  |
|  |  | added 1997/98 | 100 |  |  |
|  |  | taken 1997/98 | -20 |  |  |
|  |  | Added December 2008 - Contract R 2008 / 13 | 200 |  |  |
| 82 | a | Rock rip rap | 100 |  |  |
| 83 |  | Rock spur | 230 |  |  |
| 83 | a | Rock spur (between spurs #83 & #84) | 40 |  |  |
| 84 |  | Rock spur | 75 |  |  |
| 85 |  | Rock spur | 80 |  |  |
|  |  | added 1997/98 | 75 |  |  |
| 86 |  | Rock spur | 110 |  |  |
|  |  | added 1997/98 | 75 |  |  |
| 87 |  | Rock spur | 110 |  |  |
| 88 |  | Rock spur | 150 |  |  |
| 88 | a | Rock spur | 60 |  |  |
| 89 |  | Rock spur | 120 |  |  |
| 90 |  | Rock spur | 130 |  |  |
| 91 |  | Rock spur | 100 |  |  |
| 92 |  | Continous rock rip rap over 40 metres | 600 |  |  |
|  |  | added 1997/98 | 70 |  |  |
| 93 |  | Rock spur | 200 |  |  |
| 94 |  | Continous rock rip rap over 30 lineal metres | 600 |  |  |
| 94 | a | Rock rip rap | 400 |  |  |
| 94 | b | Rock rip rap | 200 |  |  |
|  |  | Added November 2007 | 120 |  |  |
| 95 |  | Continous rock rip rap over 40 lineal metres | 800 |  |  |
| 96 |  | Continous rock rip rap over 150 lineal metres | 2000 |  |  |
|  |  | Added December 2008 - Contract R 2008 / 13 | 100 |  |  |
|  |  | Added Aug 2010 R 2010.12 - Foster | 100 |  |  |
| 96 | a | Rock spur (between spurs #96 & #97) | 50 |  |  |
| 96 | a | Added Nov 98 | 18 |  |  |
|  |  | Added November 2007 | 60 |  |  |
| 97 |  | rock spur | 80 |  |  |
| 97 |  | Added Nov 98 | 50 |  |  |
| 97 | a | Rock spur (between spurs #97 & #98) | 50 |  |  |
| 98 |  | Rock spur | 100 |  |  |
| 99 |  | Rock spur | 160 |  |  |
| 99 | a | Added Nov 98 | 30 |  |  |
| 100 |  | Rock spur | 80 |  |  |
| 101 |  | Continous rock rip rap over 65 lineal metres | 815 |  |  |
| 102 |  | Rock spur | 80 |  |  |
|  |  | added 1997/98 | 30 |  |  |
| 103 |  | Rock spur | 80 |  |  |
| 104 |  | Rock spur | 50 |  |  |
| 105 |  | Rock spur | 100 |  |  |
|  |  | added 1997/98 | 170 |  |  |
| 105 | a | Rock rip rap | 260 |  |  |
|  |  | added 1997/98 | 80 |  |  |
| 106 |  | Rock spur | 100 |  |  |
|  |  | added 1997/98 | 100 |  |  |
| 107 |  | Rock spur | 80 |  |  |
|  |  | added 1997/98 | 100 |  |  |
| 108 |  | Rock spur | 100 |  |  |
|  |  | added 1997/98 | 100 |  |  |
| 108 | a | added 1997/98 | 60 |  |  |
| 109 |  | Rock spur | 50 |  |  |
|  |  | added 1997/98 | 50 |  |  |
| 110 |  | Rock spur | 50 |  |  |
|  |  | added 1997/98 | 10 |  |  |
| 111 |  | Continous rockwork over 70 metres | 1000 |  |  |
| 112 |  | Rock spur | 100 |  |  |
| 112 | a | Rock rip rap | 332 |  |  |
| 113 |  | Rock spur | 50 |  |  |
| 114 |  | continous rock rip rap over 80 metres | 1200 |  |  |
|  |  | Added September 2000 | 100 |  |  |
| 114 | a | Rock Spur |  |  |  |
|  |  | Added June 2006 | 60 |  |  |
| 114 | b | Rock Spur |  |  |  |
|  |  | Added June 2006 | 60 |  |  |
| 115 |  | rock spur (and concrete) | 300 |  |  |
|  |  | Added June 2006 | 80 |  |  |
| 115 | a | Rock Spur |  |  |  |
|  |  | Added June 2006 | 20 |  |  |
| 115 | b | New riprap Added November 2007 | 100 |  |  |
| 115 | c | New riprap added November 2007 | 50 |  |  |
| 116 |  | rock spur | 100 |  |  |
| 117 |  | Continuous rock work over 50 lineal metres | 630 |  |  |
| 118 |  | Rock spur | 80 |  |  |
|  |  | Added November 2007 | 60 |  |  |
| 118 | a | New spur added Aug 2010 R.2010.12 - Foster | 161 |  |  |
| 119 |  | Continuous rockwork over 100 lineal metres | 1200 |  |  |
|  |  | Added March 2005 | 40 |  |  |
|  |  | Added June 2006 | 22 |  |  |
| 119 | a | Added December 2008 - Contract R 2008 / 13 | 330 |  |  |
|  |  | Added May 2011 - R 2011.5 Westland Contractors | 216 |  |  |
| 120 |  | Rock spur | 50 |  |  |
| 120 | a | Rock Riprap |  |  |  |
|  |  | Added March 2006 | 200 |  |  |
| 121 |  | Continuous rockwork over 60 lineal metres | 900 |  |  |
|  |  | added 1997/98 | 20 |  |  |
| 121 |  | Added Nov 98 | 100 |  |  |
|  |  | Added Nov 98 | 20 |  |  |
| 122 |  | Rock spur | 150 |  |  |
| 123 |  | rock spur | 130 |  |  |
| 124 |  | rock spur | 360 |  |  |
| 125 |  | Stopbanking (Point E to F) |  |  |  |
|  |  | 2.5 metres high (average), 2:1 batters |  |  |  |
|  |  | 4 metres topwidth 2300 lineal metres |  | 51800 |  |
| D |  | LEFT BANK ABOVE ROAD BRIDGE |  |  |  |
| 127 |  | Continous rock work over 100 lineal metres | 1000 |  |  |
|  |  | Added Nov 98 | 200 |  |  |
|  |  | Added April 2012 - G.H. Foster | 400 |  |  |
|  |  | New Access Stopbank over 40 m - Kendrick |  | 1320 |  |
|  |  | Added June 2012 |  |  |  |
| 128 |  | Rock spur | 80 |  |  |
| 128 |  | Added Nov 98 | 50 |  |  |
|  |  | Added September 2000 | 30 |  |  |
| 128 | a | Riprap added May 2011- 20m - Westland Contr. | 138 |  |  |
| 129 |  | Rock spur | 50 |  |  |
|  |  | Added September 2000 | 30 |  |  |
|  |  | Added March 2006 | 20 |  |  |
| 130 |  | Continuous rock work over 50 lineal metres | 650 |  |  |
| 131 |  | Rock spur | 50 |  |  |
|  |  | Added May 2011 R2011.5 - Westland Contractors | 80 |  |  |
| 131 | a | Riprap added May 2011- 20m - Westland Contr. | 130 |  |  |
| 132 |  | rock spur | 50 |  |  |
|  |  | Added March 2006 | 180 |  |  |
|  |  | Added May 2011 R2011.5 - Westland Contractors | 130 |  |  |
| 132 | a | Rock Spur |  |  |  |
|  |  | Added March 2006 | 100 |  |  |
| 133 |  | Rock spur | 50 |  |  |
|  |  | Added May 2011 R2011.5 - Westland Contractors | 80 |  |  |
| 133 | a | Cut-off Spur |  |  |  |
|  |  | Added March 2006 | 100 |  |  |
| 134 |  | Stopbank (Point G to H) |  |  |  |
|  |  | 2.0 metres high, 4 metres topwidth |  |  |  |
|  |  | 2:1 batters, 450 lineal metres |  | 7200 |  |
| 135 |  | Rock riprap | 260 |  |  |
|  |  | Added April 2002 | 60 |  |  |
|  |  | Added Dec 2008 - Contract r 2008/13 MBD | 300 |  |  |
|  |  | Added May 2011 R2011.5 - Westland Contractors | 90 |  |  |
|  |  | Contract 2014/10 Topup riprap | 156 |  |  |
| 136 |  | Rip Rap added 1997/98 | 520 |  |  |
| 137 |  | New Spur added September 2000 | 80 |  |  |
| 138 |  | New Spur added September 2000 | 80 |  |  |
| 139 |  | New Spur added September 2000 | 80 |  |  |
| 140 |  | New Spur added September 2000 | 80 |  |  |
| 141 |  | New Spur added September 2000 | 80 |  |  |
| 142 |  | New Spur added September 2000 | 100 |  |  |
| 143 |  | New Spur added September 2000 | 80 |  |  |
| 144 |  | New Spur added September 2000 | 80 |  |  |
| 145 |  | New Spur added September 2000 | 100 |  |  |
| 146 |  | New Spur added September 2000 | 40 |  |  |
| 147 |  | New Spur added September 2000 | 40 |  |  |
| 148 |  | New Riprap added September 2000 | 275 |  |  |
| 149 |  | New Spur added June 2002 | 35 |  |  |
| 150 |  | New Spur added June 2002 | 35 |  |  |
| 150 | a | New riprap added November 2007 | 100 |  |  |
| 151 |  | New Spur added June 2002 | 35 |  |  |
| 151 | a | New riprap added November 2007 | 100 |  |  |
|  |  | Added May 2010 - Paul Steegh extra 25 metres | 180 |  |  |
|  |  | Added May 2011 - Westland Contractors (+50m) | 594 |  |  |
| 152 |  | New Spur added June 2002 | 35 |  |  |
| 153 |  | New Rock Deflector Added november 2007 | 60 |  |  |
| 155 |  | Riprap 90m | 604 |  |  |
|  |  | Summary | 44124 | 109070 | 70 |
|  |  | Unit rates | $ 28.00 | $7.50 | $27.00 |
|  |  | Calculated Costs | $1,235,472.00 | $818,025.00 | $1,890.00 |
|  |  | Total Estimated Assets as at 30 June 2014 | 2,055,387.00 |  |  |
|  |  | Add 10% Contingencies to cover Design etc | $205,538.70 |  |  |
|  |  | Add 2% for Resource Consent Costs | $ 45,218.51 |  |  |
|  |  | Total Including Contingencies | $2,306,144.21 |  |  |
| TRANSIT NEW ZEALAND WORKS NOT INCLUDED IN THE RATING DISTRICT |  |  |
| 38 |  | Rock rip rap under bridge abutment 10 |  |  |  |
|  |  | lineal metres | 300 |  |  |
| 81 |  | Continuous rockwork - 50 lineal metres, |  |  |  |
|  |  | 5 metres high, 2 metres deep | 600 |  |  |
| 126 |  | Continuous rockwork - 50 lineal metres, | 500 |  |  |

# Text boxes

13