### THE WEST COAST REGIONAL COUNCIL

WAITANGI-TAONA RIVER RATING DISTRICT

ASSET MANAGEMENT PLAN

October 2014

CONTENTS

EXECUTIVE SUMMARY	3

SECTION 1: INTRODUCTION	4

SECTION 2:	SERVICE LEVELS	8

SECTION 3:	FUNDING	11

SECTION 4: PERFORMANCE MEASURES	12

APPENDIX 1: EXPENDITURE FROM 1990	13

APPENDIX II – ASSET REGISTER AND INFRASTRUCTURE MAPS	14

## EXECUTIVE SUMMARY

Under the Local Government  Act 2002 Councils are required to develop ‘Asset Management Plans’ to demonstrate that they are managing the infrastructure for which they have responsibility.

This plan sets out the history of the scheme so there is a record of the major decisions, including expenditure. It identifies the Objective(s) of the scheme as well as the methods of monitoring the condition of the assets, and determining the annual maintenance needed to retain the service level.

The Waitangi-taona River Scheme extends from the State Highway Bridge downstream for 3.4 kilometers to the lower hill.

The area protected is predominantly dairy and dry stock farming. Community infrastructure such as roads, power and telephone lines all derive benefit from the river control system.

The Infrastructural Asset Register details all of the Scheme’s assets and their latest valuation.

## SECTION 1: INTRODUCTION

1.1	PURPOSE OF AN ASSET MANAGEMENT PLAN

This Asset Management Plan defines the objective and performance standards of the Waitangi-taona Rating District scheme for which the Regional Council has the maintenance responsibility. It also provides a basis upon which the effectiveness of maintenance performance can be measured.

This asset management plan:

- Identifies the service level for the Rating District.

- Describes the history of the rating district and identifies it’s assets.

- Describes the methods used to maintain the service level of these assets.

- Complies with the regulatory requirements of the Local Government Act 2002.

# 1.2	BACKGROUND

A large slip occurred in the headwaters of the Waitangi-taona River (Gaunt Creek) in the early 1920’s.  The State Highway Bridge was built at the same time.

In 1931, $12,000 was provided for the construction of a stopbank along the left bank downstream of the bridge to prevent the main flow of the river from leaving its course and ultimately flowing into Lake Wahapo.

In 1947 a further $12,300 was spent on raising and extending this bank.  The area protected was 500 hectares at peak flood time.  Also in 1947 the road bridge was raised by 1 metre because the waterway had been reduced by 50% due to aggradation from the slip material.  The material in some places was higher than the surrounding land.

It was pointed out in 1948 that small scale works would not “tame” the Waitangi-taona River.  As a consequence a request was made to extend the left bank stopbank.

In February 1949, 100 metres of the left bank stopbank was breached.  The previously placed willow mattresses held in place with rock and ex World War II  torpedo nets were scoured out.

In March 1955 the left stopbank breached over 80 metres.  Property, houses and sheds were flooded.  Two further floods partially destroyed the remedial works.  5,500m3 of fill was required to repair the damage.

In August 1955 a proposal to raise the left bank stopbank to provide a 2 metre freeboard was suggested.  Spur groynes (crates) were proposed.

The Westland Catchment Board reported in 1959, that to raise the bank to restore freeboard due to aggradation and carry out full rock protection would cost at least $63,000.

Also in 1959 a report to the newspaper pointed out that only 5 farms were bearing the full cost of the works, 2 of which were receiving little or no benefit and to give these 2 farms protection an extension of 3.2 kilometres of stopbank would be required at a cost of $24,000.  This could be doubled if rock work was required for erosion protection.  Some questions also arose on a comprehensive river scheme covering the right bank, but this was considered uneconomic at the time (i.e. 12.8 kilometres of stopbank being required costing a considerable sum).

By 1960 the protection works covered:

- The right bank upstream of the bridge (1,040 lineal metres of stopbanking). This was maintained by the Works Department. This work had the effect of realigning the river into a smoother more direct line leading into the State Highway Bridge.

- The left bank below the State Highway Bridge. $20,000 had been spent on this bank and maintenance was reasonably high due to aggradation.

Severe flooding in March and April 1967 caused a major breach in the left bank stopbank approximately 200 metres below the road bridge.  This breach flooded Muir’s farm and continued to flow down into Lake Wahapo which rose 3 metres above normal and flooded the main highway.  The breach was 220 metres wide and 3 metres high, resulting in Muir’s farm being abandoned.  Prior to the flood damage occurring an estimate had been prepared to strengthen the bank but as local interest was not forthcoming the proposal lapsed.

At a public meeting on 11 April 1967, it was decided to approach the Soil Conservation and Rivers Control Council for advice. The flood itself was estimated at a 5 year return period flood.

State Highway 6 was blocked by floodwaters five times in 1967.  $48,000 was spent in the first year on State Highway repairs:

Bank Protection near State Highway bridge	$4,000

Protecting bridge piles 	$10,000

Richardson Road stopbank 	$6,000

Raising bank at Lake Wahapo 	$15,000

Restoration and protection below Lake Wahapo Outlet 	$5,000

Miscellaneous	$8,000

A report was commissioned by the Ministry of Works in October 1968. The recommendations were that:

- The Westland Catchment Board be asked to prepare proposals for a Waitangi-taona River Control Scheme to direct and maintain the Upper Waitangi River on a course through Lake Wahapo.

2.	With local approval set in motion the procedure to set up a separate rating area to finance the proposal.

On 24 February 1969, NWASCO advised the Westland Catchment Board “That the new course of the Waitangi-taona River be accepted as a natural feature and the Westland Catchment Board be advised to prepare a scheme proposal for the necessary river control works”.

On 16 March 1971 the Westland Catchment Board purchased Mr Muir’s property and on 13 September 1973 a preliminary estimate of $300,000 was placed on the scheme proposal.  The estimate involved 52,000m3 of fill on the right bank and 96,000m3 of stopbanking on the left bank.  The balance of $231,000 involved rock work, creek and channel clearing, land acquisition, fencing and control weirs at Lake Wahapo. The work was to be spread over a 15 year period.

In 1976 a revised estimate was proposed. This had the effect of raising the cost to $472,000.

On 10 November 1982, the majority of ratepayers voted to request the Westland Catchment Board to proceed with a comprehensive scheme.  A provisional classification was prepared on 26 April 1983.  The Waitangi-taona Special Scheme and classification was adopted by the Westland Catchment Board on 23 May 1983 and approval to proceed with scheme works was approved by the Ministry of Works on the 31 May 1983. The design of stopbanks was based on a 800 cumecs flood event with 900mm freeboard.

With a classification in place a final scheme proposal was forwarded which involved a 3 year construction works programme.

On 19 December 1983 NWASCO approved a 70% subsidy rate for the Waitangi-taona Scheme.

Stage 1 was completed on 14 November 1984.  The works involved:

- 12,470m3 of stopbanking;

- 2,500 tonnes of rockwork;

- 576 tonnes of rubble.

The total cost of $44,140 completed by H. Langridge & Sons Ltd. Stage 2 involved the completion of right bank scheme works.  This was carried out in 1985 and involved the following:

- All weather access formation

- 3 groynes (240 tonnes)

- Rock facing (2,400 tonnes of rock – 2,000 tonnes of rubble)

- Extension of stopbank to toe of hill (1,355 metres) 15,500m3

- 1,500 lineal metres of rear drain

It is important to note that the left bank works are to be maintained solely by NZTA.

1.3 	DESCRIPTION OF ASSETS

The Rating District control works are identified in the Infrastructural Asset Register. The total replacement value of these works was $2,218,613 as at 30 June 2014.

| Asset Class | Value |
| --- | --- |
| Rock | $778,778 |
| Rock (Stockpiled) | $20,580 |
| Fill | $1,004,250 |
| Rubble | $167,266 |
| Excavation | $6,500 |
| Land | $15,594 |
| Contingency and Administration | $241,239 |
| TOTAL | $2,218,613 |

The capital value of land and buildings within the confines of the scheme is $58.3M.

1.4	MAINTENANCE EXPENDITURE

Appendix I shows expenditure since 1991. The average annual expenditure is $23,264

1.5	EXISTING STANDARD

Cross-section and flood flow analysis undertaken for the Waitangitaona scheme indicates that it is capable of containing less than 990 cumecs, which is the 2008 estimate of the 1 in 50 year return period flood with 600mm freeboard. The rating district has accepted there is a need to eventually increase the level of protection afforded by the stopbank and are considering raising its height in the medium to long term future.

## SECTION 2:	SERVICE LEVELS

2.1	OBJECTIVE

The objective of the Waitangi-taona Rating District is to reduce bank erosion and flooding on the right bank between the State Highway bridge and lower hill of the Waitangi-taona River.

2.2	MAINTENANCE PROGRAMME

An annual maintenance programme will be prepared each year in consultation with the Wanganui ratepayer sub committee prior to adoption by the Council for inclusion in the Annual Plan.

In preparing the annual maintenance programme consideration will be given to:

- works requiring immediate repair.

- works anticipated as being required given a ‘normal’ season.

- flexibility to meet unbudgeted damages.

An annual report will be presented to the Rating District outlining the condition of the scheme assets and maintenance works and expenditure required for the coming financial year.

Stopbanks

Stopbanks are man made structures generally running parallel to the flow of the river that are built to raise the bank level and hence increase the capacity of the river. They are usually constructed of compacted river gravels with a grass cover and do not have the strength to resist the erosive forces of a river in flood without adequate bank protection works in place.

Maintenance includes repair of any scouring, vegetation removal to facilitate access, control of stock to prevent damage to stopbank batter slopes, topping up of stopbanks as required to maintain stopbank capacity in terms of design.

Stopbanks can potentially be damaged by:

- Failure of a training groyne such as a rock retard which can allow the full force of the river to suddenly run along a relatively unprotected stopbank, and cause scouring of stopbanks in excess of 50 metres in length

- Overtopping: Stopbanks are generally not designed to sustain overtopping. They may however be capable of sustaining minor overtopping for a short duration in flows not exceeding 100mm in depth over the top of the bank. Overtopping of durations greater than an hour may scour the back batter resulting in failure of the structure, it is therefore important to ensure there is an even and strong vegetation cover on the landward batter.

- Piping: Flow through porous bank or foundation material can wash out fines leading to a collapse.

- Stock and Vehicles: Can remove cover and wear ruts in surface resulting in weakness.

- Construction: Construction of pipelines cables under stopbanks as well as holes on top of stopbanks can weaken the structure. Drainage channels should not be located at the toe of stopbanks.

- Earthquake: Stopbanks can be damaged in the event of an earthquake by cracking vertical or horizontal displacement, or by liquefaction of the foundation material.

Erosion Control / River Training

Erosion control works consist of rock placed in continuous riprap, spur groynes, stub groynes, strongheads, hook groynes, and in river training retards. These are built to provide protection to stopbanks from the river’s erosive forces during floods, by training the river into a stable pattern or by reducing velocities along stopbanks using stub rock groynes.

Only limited river training is carried out by way of channel improvements by diversion or extraction of river gravels. This is generally accepted as only having a limited and temporary influence on the channel hydraulics (performance).

Erosion control structures are constructed to absorb the energy of the river, to control the alignment of the flow of the rivers, and subsequently give the required protection to stopbanks and natural banks. Because of this they are the areas with the major exposure to damage. 	The meander of a river can change significantly by floods of only moderate duration.  This can result in an acute angle of attack of protection structures resulting in damage which is disproportional to the flood discharge. Likewise erosion control works already weakened from previous floods may sustain damage disproportionate to the flood discharge.

It is very important to ensure damage to bank protection structures is undertaken swiftly and to ensure:

- Rock training walls are kept to the required height to lessen failure.

- Any slumping of rock off strongpoints, spur groynes and rip rap are topped up.

- Rock is of a durable nature, angular and of the correct grading size.

Drainage and Creek Channels

Drains and Creeks are used to discharge runoff water from land to river systems. Drains are man made structures usually created to improve land use. Creeks, which are natural channels are used in a similar manner. To maintain a drain’s channel capacity it is essential to:

- Keep drains and channels clear of siltation, weed and vegetation growth

- Control stock around the banks and repair any stock damage to banks and batters.

2.3	DAMAGE EXPOSURE

River control works are constructed in a very high energy environment with the purpose of resisting and absorbing some of that energy.  It is considered that no matter what the standard of maintenance carried, it is inevitable that damage will occur to structures.

An assessment of maximum damage potential was derived from estimating the damage ratios and costs for three flood events and is in vicinity of $400,000.

| FLOOD EVENT SIZE | VALUE | DAMAGE RATIO | DAMAGE EXPOSURE |
| --- | --- | --- | --- |
| 20 Year | $2,218,613 | 10% | $221,861 |
| 100 Year | $2,218,613 | 20% | $443,722 |
| 500 Year | $2,218,613 | 25% | $554,653 |

## SECTION 3:	FUNDING

3.1	MAINTENANCE

Maintenance is funded by targeted rates, the level of rating being determined each year in the Annual Plan process following:

- Preparation of an annual works programme and corresponding budget.

- Consultation with Rating District.

- Adoption of draft programme and budget by Council.

- Adoption of final Annual Plan by Council.

3.2	DAMAGE REPAIRS

Routine damage repairs are funded by a combination of:

- carrying out work as scheduled in annual works programme.

- reprioritising works identified in the annual works programme.

- use of financial reserves.

Major damage repairs would be funded by loans raised by the Council and repaid by targeted rating over a number of years.

3.3	FINANCIAL RESERVES

Financial reserves are held within each rating districts account to provide the following.

- meet the costs of unscheduled works.

- enable an immediate response to flood damage repairs.

- prevent major fluctuation in rating levels annually.

The level of financial reserves held in each rating account is determined by the assessment of risk damage and the need for unprogrammed works.

3.4	DEPRECIATION

Rating District schemes are designed to be maintained in perpetuity by constantly repairing and replacing component parts which are damaged by the constant wear and tear. Because there is a constant cycle of replacement of elements of the infrastructure, depreciation of the value of the assets is not appropriate and funding of depreciation is not necessary. This approach is consistent with the NZ Infrastructure Asset Valuation and Depreciation Guidelines (Section 5.4.4).

## SECTION 4: PERFORMANCE MEASURES

The overall performance measure is that the infrastructure assets are maintained to meet their service levels at all times.

The following procedures will be adopted to ensure the adequacy of maintenance.

Annually

- Produce annual works report for the rating district to include type of work to be undertaken, quantities, location and costs.

- Organise contracts for agreed scheme work, oversee contract completion and report to Council.

(iii)	Report on works undertaken during the previous financial period to the rating district ratepayers and Council.

Performance Measure

No reports of stopbanks or erosion protection works requiring repairs without an agreed programme of remedial work in progress.

Triennially

(i)	Re-fly aerial photographs of the area, analysing these photographs to assess changes in river meander patterns that could impact on Rating District Assets.

(ii)	Re-measure cross section river profiles to determine whether the riverbed is stable, or aggrading, and to identify management issues or options.

(iii)	Revaluation of the asset schedule to include any additional rock placed on stopbanks and bank protection works over the three year period.

(iv)	Review this Asset Management Plan

Performance Measure

Report to Council and ratepayers on revaluation of assets and the Plan review.

## APPENDIX 1: EXPENDITURE FROM 1990

| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 9,562 | 0 | 3,824 | 13,395 | 13,548 | 34,953 | 11,067 | 13,406 |
| 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 |
| 17,995 | 14,449 | 22,140 | 3,305 | 3,499 | 1,642 | 3,203 | 30,078 |
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 |
| 2,360 | 46,240 | 9.670 | 105,535 | 91,137 | 24,422 | 67,662 | 4,064 |
| 2014 |  |  |  |  |  |  |  |
| 44,115 |  |  |  |  |  |  |  |

| Total Expenditure | $ 581,611 |
| --- | --- |
| Average Expenditure | $ 23,264 |
| Average Expenditure as a % of Asset Value | 1.07% |

As at 30 June 2014, the value of the Waitangitaona Rating District Scheme assets is $2,218,613

APPENDIX II – ASSET REGISTER AND INFRASTRUCTURE MAPS

|  |  | WAITANGI-TAONA RATING DISTRICT |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Infrastructural Assets - Amended to 30 June 2014 |  |  |  |  |  |
|  |  | REFER TO PLAN NO. 892/42 |  |  |  |  |  |
|  |  |  | Rock | Stockpiles | Fill | Rubble | Excavation |
|  |  |  | tonne | tonne | m³ | tonne | m³ |
| 1 |  | Rock spur groyne | 100 |  |  |  |  |
| 1 | a | added 1997/98 | 336 |  |  |  |  |
| 2 |  | Rock spur groyne | 100 |  |  |  |  |
| 3 |  | 50 metres of rip rap | 600 |  |  |  |  |
|  |  | Added October 2005 | 1192 |  |  |  |  |
| 4 |  | Rock spur groyne | 160 |  |  |  |  |
| 4 | a | added 1997/98 | 400 |  |  |  |  |
| 5 |  | Rock rip rap 80 metres | 1486 |  |  |  |  |
| 6 |  | 250 metres of rock rip rap | 2500 |  |  |  |  |
| 7 |  | Rock spur groyne | 100 |  |  |  |  |
| 7 | a | Rock rip rap | 50 |  |  |  |  |
| 8 |  | Spur groyne | 100 |  |  |  |  |
| 8 | a | Rock rip rap | 50 |  |  |  |  |
| 9 |  | Spur groyne | 100 |  |  |  |  |
| 10 |  | 250 lineal metres of rip rap | 3500 |  |  |  |  |
| 11 |  | 180 lineal metres of stopbank |  |  | 8500 |  |  |
|  |  | 2:1 batters, 4 metres high, (Average) |  |  |  |  |  |
|  |  | 4 metres topwidth |  |  |  |  |  |
| 12 |  | Spur groyne | 50 |  |  |  |  |
| 13 |  | 15 metres lineal rip rap | 150 |  |  |  |  |
|  |  | Added march 2004 | 150 |  |  |  |  |
| 14 |  | 8 x 50 tonnes spur groynes | 400 |  |  |  |  |
| 15 |  | 36 lineal metres of rock along face of | 150 |  |  |  |  |
|  |  | deflector bank |  |  |  |  |  |
|  |  | Added March 2004 | 250 |  |  |  |  |
| 16 |  | 15 lineal metres rip rap on end of deflector |  |  |  |  |  |
|  |  | bank | 500 |  |  |  |  |
| 17 |  | 30 lineal metres rock retard | 900 |  |  |  |  |
| 18 |  | 130 lineal metres of deflector bank |  |  | 6500 |  |  |
| 18 | a | Added February 1999 | 100 |  |  |  |  |
| 18 | b | Added February 1999 | 100 |  |  |  |  |
| 18 | c | Added February 1999 | 100 |  |  |  |  |
| 19 |  | 3 x 50 tonnes spur groynes | 150 |  |  |  |  |
|  |  | Added February 1999 | 150 |  |  |  |  |
| 20 |  | Spur groyne | 20 |  |  |  |  |
| 21 |  | 5 x 100 tonnes spur groynes along deflector |  |  |  |  |  |
|  |  | bank | 500 |  |  |  |  |
|  |  | Added March 2004 | 252 |  |  |  |  |
| 22 |  | 60 lineal metres of rip rap along deflector bank | 1300 |  |  |  |  |
|  |  | Added April 2011 - Arnold Contracting | 75 |  |  |  |  |
|  |  | Added November 2014 | 594 |  |  |  |  |
| 23 |  | 40 lineal metres rock retard at end of deflector |  |  |  |  |  |
|  |  | bank | 1200 |  |  |  |  |
|  |  | Added December 2000 | 250 |  |  |  |  |
|  |  | Added January 2002 | 100 |  |  |  |  |
| 23 | a | Rock Riprap Added December 2000 | 300 |  |  |  |  |
| 24 |  | 130 lineal metres of deflector bank 4 metres high, |  |  |  |  |  |
|  |  | (Average), 2:1 batters |  |  | 6500 |  |  |
|  |  | Added December 2000 over 50 metres |  |  | 1000 |  |  |
| 25 |  | 55 lineal metres of rip rap | 550 |  |  |  |  |
| 26 |  | 4 x 200 tonnes spur groynes | 800 |  |  |  |  |
| 27 |  | 20 lineal metres of rip rap along deflector | 300 |  |  |  |  |
|  |  | Added February 2009 - Contract R 2009/2 | 500 |  |  |  |  |
|  |  | Added February 2009 - Contract R 2009/2 |  |  |  | 150 |  |
| 28 |  | 20 lineal metres of rip rap along deflector | 1150 |  |  |  |  |
| 29 |  | 55 lineal metres rock retard at end of deflector |  |  |  |  |  |
|  |  | bank | 1200 |  |  |  |  |
|  |  | Added December 2000 | 250 |  |  |  |  |
|  |  | Added October 2005 | 300 |  |  |  |  |
|  |  | Added August 2007 | 200 |  |  |  |  |
| 29 | a | Rock Riprap Added December 2000 | 300 |  |  |  |  |
| 30 |  | 150 lineal metres stopbank |  |  |  |  |  |
|  |  | 5 metre topwidth 2:1 batters 4m high |  |  |  |  |  |
|  |  | (Average) |  |  | 8500 |  |  |
|  |  | Added December 2000 - over 50 metres |  |  | 1500 |  |  |
| 31 |  | Stopbank faced with rock rubble |  |  |  |  |  |
|  |  | N.B Rock in Items 26, 27 & 28 overlaying rubble. |  |  |  | 1000 |  |
| 32 |  | Rock stockpiles (Private Stockpile placed by Fergusons) |  | 500 |  |  |  |
|  |  | Removed by Fergusons Approx 2000) |  | -500 |  |  |  |
|  |  | Added August 2007 |  | 500 |  |  |  |
| 33 |  | 30 lineal metres of stopbank faced with rubble, 3 |  |  |  |  |  |
|  |  | metres high (Average), 2:1 batters, 4 metres |  |  |  |  |  |
|  |  | topwidth |  |  | 1000 | 100 |  |
|  |  | Added October 2005 | 500 |  |  | 50 |  |
|  |  | Added August 2007 | 100 |  |  |  |  |
| 33 | a | Riprap added February 1999 - over 60 metres | 250 |  |  |  |  |
|  |  | Added August 2007 - Over 50 metres | 400 |  |  |  |  |
| 34 |  | 5 x 40 tonnes spur groynes | 200 |  |  |  |  |
|  |  | Added February 1999 | 150 |  |  |  |  |
|  |  | Added February 2009 - Contract R 2009/2 | 44 |  |  |  |  |
| 35 |  | 2 x 100 tonnes spur groynes | 200 |  |  |  |  |
|  |  | Added February 1999 | 60 |  |  |  |  |
|  |  | Destroyed March 2011- Recover to # 35a - Arnold | -260 |  |  |  |  |
| 35 | a | Rip Rap added 1997/98 | 696 |  |  |  |  |
|  |  | Added Contract R 2009/2 - February 2009 | 500 |  |  |  |  |
|  |  | Added ex # 35 - March 2011 - Arnold | 260 |  |  |  |  |
| 36 |  | 50 lineal metres stopbank |  |  |  |  |  |
|  |  | 3 metres high |  |  |  |  |  |
|  |  | 4 metres topwidth |  |  | 1500 |  |  |
|  |  | Extend by 50m Added March 2004 |  |  | 1500 |  |  |
|  |  | Extend by 50m Added March 2004 | 372 |  |  |  |  |
|  |  | Rubble added March 2004 |  |  |  | 345 |  |
|  |  | Added April 2011ex S/P # 43 - Arnold Contracting | 20 |  |  |  |  |
| 37 |  | Main stopbank |  |  |  |  |  |
|  |  | Point A to Point B |  |  |  |  |  |
|  |  | 2,450 lineal metres |  |  |  |  |  |
|  |  | Average height 3 metres |  |  |  |  |  |
|  |  | 2:1 batters, 4 metres topwidth |  |  | 76500 |  |  |
| 38 |  | Main stopbank |  |  |  |  |  |
|  |  | Point B to Point C |  |  |  |  |  |
|  |  | 550 lineal metres |  |  |  |  |  |
|  |  | Average height 2 metres |  |  |  |  |  |
|  |  | Topwidth 3 metres |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  | 7000 |  |  |
| 39 |  | Seepage Drain |  |  |  |  |  |
|  |  | Point D to E |  |  |  |  |  |
|  |  | 1,100 lineal metres of drain |  |  |  |  |  |
|  |  | 2 metres bottom width |  |  |  |  |  |
|  |  | 0.5 metres deep (Average) |  |  |  |  |  |
|  |  | 1.5:1 batter slopes |  |  |  | 300 | 1,500 |
| 40 |  | Seepage Drain |  |  |  |  |  |
|  |  | Point E to F |  |  |  |  |  |
|  |  | 950 lineal metres |  |  |  |  |  |
|  |  | 1 metres bottom width |  |  |  |  |  |
|  |  | 1.5 metres deep (Average) |  |  |  |  |  |
|  |  | 1.5 to 1 batter slopes |  |  |  |  | 5000 |
| 41 |  | Land purchased December 1994 as part of Scheme |  |  |  |  |  |
| 42 |  | Construct new deflector over 190m |  |  |  |  |  |
|  |  | 4m top width, 2:1 batters - Added March 2004 | 956 |  | 5500 | 1271 |  |
|  |  | Added September 2009 - Contract R 2009/13 - Arnold | 200 |  |  | 750 |  |
|  |  | Extend Deflector - 150 metres - November 2009 - MBD |  |  | 2700 |  |  |
|  |  | Add riprap-160 metres-Contract R 2009/20 - MBD 11.09 | 1750 |  |  | 702 |  |
|  |  | Added January 2012 - Westland Contractors (over 300 m) | 2358 |  | 5700 | 918 |  |
|  |  | Added November 2013 | 1480 |  |  | 760 |  |
| 43 |  | New Stockpile Added upstream of #42 - August 2007 |  | 500 |  |  |  |
|  |  | Deducted April 2011 to # 36 - Arnold Contracting |  | -20 |  |  |  |
| 44 |  | New Spur Added August 2007 | 100 |  |  |  |  |
| 45 |  | New Spur Added August 2007 | 100 |  |  |  |  |
| 46 |  | New Spur Added August 2007 | 100 |  |  |  |  |
| 47 |  | New Spur Added August 2007 | 100 |  |  |  |  |
| 48 |  | New Spur Added August 2007 | 100 |  |  |  |  |
| 49 |  | New Spur Added August 2007 | 100 |  |  |  |  |
| 50 |  | New riprap over 145 metres added - Arnold - R 2010.8 | 296 |  |  | 790 |  |
| 51 |  | New Spur Added April 2010 - Arnold - R 2010.8 | 200 |  |  |  |  |
| 52 |  | New toe rock Added April 2011 - Arnold | 596 |  |  | 467 |  |
|  |  | Summary | 35993 | 980 | 133900 | 7603 | 6500 |
|  |  | Unit Rates | $ 22.00 | $ 21.00 | $ 7.50 | $ 22.00 | $ 1.00 |
|  |  | Calculated Costs | $ 791,846.00 | $ 20,580.00 | $ 1,004,250.00 | $ 167,266.00 | $ 6,500.00 |
|  |  | Total Estimated Assets as at 30 June 2014 | $ 1,990,442.00 |  |  |  |  |
|  |  | Add 10% Contingencies to cover Design etc | 199,044.20 | 242,833.92 |  |  |  |
|  |  | Add 2% for Resource Consent Costs | 43,789.72 |  |  |  |  |
|  |  | Total Including Contingencies | $ 2,233,275.92 |  |  |  |  |