THE WEST COAST REGIONAL COUNCIL

INCHBONNIE RATING DISTRICT

ASSET MANAGEMENT PLAN

October 2014

CONTENTS

EXECUTIVE SUMMARY	3

SECTION 1: INTRODUCTION	4

SECTION 2: SERVICE LEVELS	6

SECTION 3: FUNDING	8

SECTION 4: PERFORMANCE MEASURES	9

APPENDIX 1: WORKS EXPENDITURE FROM 1991	10

APPENDIX II – ASSET REGISTER AND INFRASTRUCTURE MAPS	11

### EXECUTIVE SUMMARY

Under the Local Government  Act 2002 Councils are required to develop ‘Asset Management Plans’ to demonstrate that they are managing the infrastructure for which they have responsibility.

This plan sets out the history of the scheme so there is a record of the major decisions, including expenditure. It identifies the Objective(s) of the scheme as well as setting out the methods of monitoring the condition of the assets, and determining the annual maintenance needed to retain the agreed service level.

Refer also to the Infrastructural Asset Register which details all of the Scheme’s assets and their latest valuation.

The Inchbonnie Rating district covers that area of the right bank frontage of the Taramakau River commencing at a point approximately 3.2 kilometres downstream of the Sir Stanley Gooseman Bridge, to a point, a further 3.2 kilometres downstream.

The area protected is predominantly dairy farming with some horticulture and dry stock farming. Many community infrastructures such as roads, power and telephone lines all derive benefit from the river control system.

### SECTION 1: INTRODUCTION

1.1	PURPOSE OF AN ASSET MANAGEMENT PLAN

This Asset Management Plan defines the objectives and performance standards of the Inchbonnie Rating District scheme for which the Regional Council has the maintenance responsibility. It also provides a basis upon which the effectiveness of maintenance performance can be measured.

This asset management plan:

- Identifies the service level for the Rating District.

- Describes the history of the rating district and identifies it’s assets.

- Describes the methods used to maintain the service level of these assets.

- Complies with the regulatory requirements of the Local Government Act 2002.

# 1.2	BACKGROUND

With the Taramakau River overflowing into the Orangipuku River at Inchbonnie from time to time in the early 1900’s, the threat of a “break-through” to Lake Brunner has given cause for concern for a considerable period. This concern has not only been for the Inchbonnie farming area, but also for the potential effect of increased flood flows on those areas including Lake Brunner, Arnold River and Grey Valley lands and the Town of Greymouth and associated environs.

Prior to the 1940’s, the Orangipuku River had been flowing parallel to the Taramakau River for approximately 2.5 kilometres. Erosion had occurred on the right bank of the Taramakau River and had increased the threat of a break through and had necessitated minor protection works being placed from time to time. Although sporadic, these works contained any immediate threat, but the need for a more comprehensive scheme had been long recognised, with an investigation for such a scheme being carried out as early as 1907.

On 12 February 1946, floodwaters flowed from the Taramakau River into the Orangipuku River causing serious problems. On 8 October 1946 the area was inspected by the Public Works Department and on 21 October 1946 a proposal to erect a stopbank along the right bank of the Taramakau River adjacent to the Orangipuku River was forwarded. The total cost was $32,000 ($25,600 from the Soils Council and $6,400 from local contributions. In addition both the Railways Department and the State Hydro Department were to pay $1,000 each)

On 27 March 1951, 12 local ratepayers agreed to pay $200 per year for 10 years, Greymouth Harbour Board $150 per year, Grey Borough Council $150 per year and the Grey County Council $200 per year to service a loan to carry out works.

On 21 June 1951 a description of the original proposed classification was prepared by the Westland Catchment Board.

In June 1951, a combination of tree and rock protection works were proposed to halt erosion (1,400 tonnes of rock was proposed). Permission was gained to extract the rock from McArthur’s Quarry.

On 31 August 1953 it was reported that rapid deterioration of the main Taramakau channel had occurred resulting in a net channel degradation of approximately 2 metres.  A new estimate was prepared at a cost of $50,000.

On 28 October 1953, the Minister of Public Works approved the construction of 80 metres of rockwork and 60 metres of tree protection.

On 30 January 1958 it was reported that the erosion problem on the Taramakau was so acute that only 5 metres of undisturbed land remained between the two rivers.   Emergency works were carried out until a major scheme plan was produced.

An engineering report was prepared on 23 March 1959. This involved the construction of 2.5 kilometres of new stopbanking, raising and strengthening 1.2 kilometres of existing stopbanking, 2.5 kilometres of new rock rip rap, and channel work involving the diversion of the upper section of the Orangipuku River into the Taramakau River.  The total estimated cost being $112,000.

After local meetings had indicated ratepayer support a Partial Scheme involving $44,000 was approved. This involved some 900 metres of rock riprap, and the raising and strengthening of the stopbanking where freeboard was inadequate. The proposed rating area covered an area of 2,108 hectares with a total Capital Value of $82,000.

On 3 August 1959 the NZ Soil Conservation and River Control Council granted approval on a 3:1 subsidy basis. The work involved 17,300 tonnes of rock, 9,000 cubic metres of fill for stopbanking and 3,200 tonnes of “topping-up” rock.

The classification for the Inchbonnie Rating District was finally approved by the Westland Catchment Board on 31 July 1959.

1.3 	DESCRIPTION OF ASSETS

The Rating District assets consist of all those works outlined in the Infrastructural Asset Register. The total replacement value of these works was $2.795M as at June 2014.

The capital value of land and buildings within the confines of the scheme is $23.8M.

| Asset Class | Value |
| --- | --- |
| Rock | $1,469,974 |
| Fill | $879,187 |
| Rubble | $22,220 |
| Rock (Stockpiled) | $18,900 |
| Culverts | $31,502 |
| Contingency and Administration | $303,915 |
| TOTAL | $2,795,023 |

Note that a 10% contingency to cover design and a 2% estimate for administration of the work including resource consent costs has been added to more fairly indicate total replacement costs.

1.4	MAINTENANCE EXPENDITURE

Appendix I shows expenditure since 1991. The average annual expenditure is $34,230.

1.5	EXISTING STANDARD

The stopbank has been built to contain 2,620m3/s plus 900mm freeboard (which is the current modeled estimate of a 400 year flow).

### SECTION 2: SERVICE LEVELS

2.1	OBJECTIVES

The objectives of the Inchbonnie Rating District are:

- To reduce bank erosion and flooding between the Upper and Lower extremities of the Inchbonnie Rating District protecting the farms and

- Reduce the risk of the Taramakau River breaking through into the Orangipuku River which would enable it to then flow into Lake Brunner and on into the Grey River.

The stopbank has been built to contain 2,620m3/s plus 900mm freeboard (which is the current modelled estimate of a 400 year flow).

2.2	MAINTENANCE PROGRAMME

An annual maintenance programme will be prepared each year in consultation with the rating district spokesman prior to consideration by the Rating District ratepayers and adoption by the Council in the Annual Plan.

In preparing the annual maintenance programme consideration will be given to:

-	an inspection to identify works requiring immediate repair.

-	works anticipated as being required given a ‘normal’ season.

-	flexibility to meet unbudgeted damages.

Stopbanks

Stopbanks are man made structures generally running parallel to the flow of the river that are built to raise the bank level and hence increase the capacity of the river. They are usually constructed of compacted river gravels with a grass cover and do not have the strength to resist the erosive forces of a river in flood without adequate bank protection works in place.

Maintenance includes repair of any scouring, vegetation removal to facilitate access, control of stock to prevent damage to stopbank batter slopes, topping up of stopbanks as required to maintain stopbank capacity in terms of design.

Stopbanks can potentially be damaged by:

- Failure of a training groyne which allows the full force of the river to suddenly run along a relatively unprotected stopbank, and cause scouring of stopbanks in excess of 50 metres in length

- Overtopping: Stopbanks may be capable of sustaining minor overtopping for a short duration not exceeding 100mm depth over the top of the bank. Overtopping of durations greater than an hour may scour the back batter resulting in failure of the structure, it is therefore important to ensure there is an even and strong vegetation cover on the landward batter.

- Piping: Flow through porous bank or foundation material can wash out fines leading to a collapse.

- Stock and Vehicles: Can remove cover and wear ruts in surface resulting in weakness.

- Construction: Construction of pipelines cables under stopbanks as well as holes on top of stopbanks can weaken the structure. Drainage channels should not be located at the toe of stopbanks.

- Earthquake: Stopbanks can be cracked by vertical or horizontal displacement, or by liquefaction of the foundation material.

Erosion Control / River Training

Erosion control works consist of rock placed in continuous riprap, spur groynes, stub groynes, strongheads, hook groynes, and in river training retards. 	Erosion control and river training structures are built to provide protection to stopbanks and natural bush from the rivers erosive forces during floods by training the river into a stable pattern or reduce velocities along stopbanks using stub rock groynes.

Only limited river training is carried out by way of channel improvements by diversion or extraction of river gravels. This is generally accepted as only having a limited and temporary influence on the channel hydraulics (performance).

Erosion control structures are constructed to absorb the energy of the river, to control the alignment of the flow of the rivers, and subsequently give the required protection to stopbanks and natural banks. Because of this they are the areas with the major exposure to damage. 	The meander of a river can change significantly by floods of only moderate duration.  This can result in an acute angle of attack of protection structures resulting in damage which is disproportional to the flood discharge. Likewise erosion control works already weakened from previous floods may sustain damage disproportionate to the flood discharge.

It is very important to ensure damage to bank protection structures is undertaken swiftly and to ensure:

- Rock training walls are kept to the required height to lessen failure.

- Any slumping of rock off strongpoints, spur groynes and rip rap are topped up.

- Rock is of a durable nature, angular and of the correct grading size.

2.3	DAMAGE EXPOSURE

River control works are constructed in a very high energy environment with the purpose of resisting and absorbing some of that energy.  It is considered that no matter what the standard of maintenance carried, it is inevitable that damage will occur to structures.

An assessment of maximum damage potential was derived from estimating the damage ratios and costs for three flood events and is in vicinity of $400,000.

| FLOOD EVENT SIZE | VALUE | DAMAGE RATIO | DAMAGE EXPOSURE |
| --- | --- | --- | --- |
| 20 Year | $2,795,023 | 10% | $279,502 |
| 100 Year | $2,795,023 | 20% | $559,004 |
| 500 Year | $2,795,023 | 20% | $559,004 |

### SECTION 3: FUNDING

3.1	MAINTENANCE

Maintenance is funded by targeted rates, the level of rating being determined each year in the Annual Plan process following:

- Preparation of an annual works programme and corresponding budget.

- Consultation with Rating District.

- Adoption of draft programme and budget by Council.

- Adoption of final Annual Plan by Council.

3.2	DAMAGE REPAIRS

Routine damage repairs are funded by a combination of:

- carrying out work as scheduled in annual works programme.

- reprioritising works identified in the annual works programme.

- use of financial reserves.

Major damage repairs would be funded by loans raised by the Council and repaid by targeted rating over a number of years.

3.3	FINANCIAL RESERVES

Financial reserves are held within each rating districts account to provide the following.

- meet the costs of unscheduled works.

- enable an immediate response to flood damage repairs.

- prevent major fluctuation in rating levels annually.

The level of financial reserves held in each rating account is determined by the assessment of risk damage and the need for unprogrammed works.

3.4	DEPRECIATION

River control schemes are designed to be maintained in perpetuity by constantly repairing and replacing component parts which are damaged by the constant wear and tear. Because there is a constant cycle of replacement of elements of the infrastructure, depreciation of the value of the assets is not appropriate and funding of depreciation is not necessary. This approach is consistent with the NZ Infrastructure Asset Valuation and Depreciation Guidelines (Section 5.4.4).

### SECTION 4: PERFORMANCE MEASURES

The overall performance measure is that the infrastructure assets are maintained to meet their service levels at all times.

The following procedures will be adopted to ensure the adequacy of maintenance.

Annually

- Produce annual works report for the rating district to include type of work to be undertaken, quantities, location and costs.

- Organise contracts for agreed scheme work, oversee contract completion and report to Council.

(iii)	Report on works undertaken during the previous financial period to the rating district ratepayers and Council.

Performance Measure

No reports of stopbanks or erosion protection works requiring repairs without an agreed programme of remedial work in progress.

Triennially

(i)	Re-fly aerial photographs of the area, analysing these photographs to assess changes in river meander patterns that could impact on Rating District Assets.

(ii)	Re-measure cross section river profiles to determine whether the riverbed is stable, or aggrading, and to identify management issues or options.

(iii)	Revaluation of the asset schedule to include any additional rock placed on stopbanks and bank protection works over the three year period.

(iv)	Review this Asset Management Plan

Performance Measure

Report to Council and ratepayers on revaluation of assets and the Plan review.

### APPENDIX 1: WORKS EXPENDITURE FROM 1991

| 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 12,904 | 4,801 | 10,541 | 6,148 | 5,517 | 8,934 | 1,563 | 16,811 |
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 |
| 57,623 | 37,193 | 1,287 | 34,745 | 25,497 | 985 | 20,994 | 4,996 |
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 |
| 60,894 | 41,841 | 297,093 | 276,597 | 27,654 | 4,240 | 0 | 0 |

| Asset Value | $ 2,795,023 |
| --- | --- |
| Total Expenditure | $ 958,858 |
| Average Expenditure | $39,952 |
| Average Expenditure as a % of Asset Value | 1.42% |

As at 30 June 2014, the value of the Inchbonnie Rating District Scheme assets was $2,795,023

###### APPENDIX II – ASSET REGISTER AND INFRASTRUCTURE MAPS

| INCHBONNIE RATING DISTRICT |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Infrastructural Assets - Amended to 30 June 2014 |  |  |  |  |  |  |  |  |
| Refer to Drawing No. A2/911/93 |  |  |  |  |  |  |  |  |
|  |  |  | Rock | Fill | Rubble | Stockpile | Culverts | AP 65 | AP 40 | Floodgates |
|  |  |  | Tonnes | m³ | Tonnes | Tonnes | $ | m3 | m3 | $ |
| A |  | STOPBANKING |  |  |  |  |  |  |  |  |
| 1 | a | Point A to Point B (lower end) Upgraded Sept '09 |  |  |  |  |  |  |  |  |
|  |  | 777.50 lineal metres, 8 metres top width (Road) |  |  |  |  |  |  | 366 |  |
|  |  | 3:1 batters, average 3 metres high (Includes ramps) |  | 21695 |  |  |  | 820 | 490 |  |
| 1 | b | Point B to Point C (upstream) Upgraded Sept '09 |  |  |  |  |  |  |  |  |
|  |  | 1675 lineal metres, 4 metres topwidth |  |  |  |  |  |  |  |  |
|  |  | 3:1 batters, 3.5 metres average height |  |  |  |  |  |  |  |  |
|  |  | (includes ramps) |  | 68190 |  |  |  | 700 |  |  |
| 1 | c | Point C to Point D (to Road) Upgraded Sept '09 |  |  |  |  |  |  |  |  |
|  |  | 696.5 lineal metres, 4 metres topwidth |  |  |  |  |  |  |  |  |
|  |  | 3:1 batters, 1.5 metres average height |  |  |  |  |  |  |  |  |
|  |  | (includes ramps) |  | 20,290 |  |  |  | 280 |  |  |
| B |  | OTHER STRUCTURES |  |  |  |  |  |  |  |  |
| 2 |  | Old Deflector Groyne |  |  |  |  |  |  |  |  |
|  |  | 100 lineal metres, 3 metre topwidth, |  |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters, Average 3.5 metres high, |  |  |  |  |  |  |  |  |
|  |  | 1000 tonne of rock around point | 1000 | 2900 |  |  |  |  |  |  |
| 3 |  | Deflector Groyne |  |  |  |  |  |  |  |  |
|  |  | 100 metres lineal, 3 metre topwidth, |  |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters, 3.5 metres high |  | 2900 |  |  |  |  |  |  |
|  |  | Continuous Rock (allow 3.5m) |  |  |  |  |  |  |  |  |
|  |  | high, 2 metres underground |  |  |  |  |  |  |  |  |
|  |  | (i.e 12 metres slope) | 2000 |  |  |  |  |  |  |  |
| 4 |  | Continuous Rock rip rap |  |  |  |  |  |  |  |  |
|  |  | 340 lineal metres, 2:1 batters |  |  |  |  |  |  |  |  |
|  |  | 3.5 metres high, 2 metres buried |  |  |  |  |  |  |  |  |
|  |  | 1 metre thick (12 metre slope) | 7000 |  |  |  |  |  |  |  |
|  |  | added 1997/98 | 350 |  |  |  |  |  |  |  |
|  |  | Added March 2011-MBD | 150 |  |  |  |  |  |  |  |
| 5 |  | Continuous Rock rip rap |  |  |  |  |  |  |  |  |
|  |  | 500 metres lineal, 4 metres high |  |  |  |  |  |  |  |  |
|  |  | 2:1 batters, 2 metres buried |  |  |  |  |  |  |  |  |
|  |  | 1 metre thick (13 metre slope) | 11000 |  |  |  |  |  |  |  |
|  |  | added 1997/98 | 350 |  |  |  |  |  |  |  |
|  |  | added october 99 | 300 |  |  |  |  |  |  |  |
|  |  | Topped up Oct '09 - MBD Contracting Ltd | 100 |  |  |  |  |  |  |  |
| 6 |  | Rock return up creek bank |  |  |  |  |  |  |  |  |
|  |  | 30 metres lineal, 2:1 batters |  |  |  |  |  |  |  |  |
|  |  | 5 metres high, 2 metres buried | 700 |  |  |  |  |  |  |  |
|  |  | Topped up Oct '09 - MBD Contracting Ltd | 200 |  |  |  |  |  |  |  |
| 6 | a | Rubble weir added - Oct '09 - MBD Contracting |  |  | 60 |  |  |  |  |  |
| 7 |  | Rock return up Creek Bank |  |  |  |  |  |  |  |  |
|  |  | 40 metres lineal, 5 metres high |  |  |  |  |  |  |  |  |
|  |  | 2:1 batters, 2 metres buried |  |  |  |  |  |  |  |  |
|  |  | 1 metre thick | 1000 |  |  |  |  |  |  |  |
| 8 |  | Continuous Rock rip rap |  |  |  |  |  |  |  |  |
|  |  | 800 metres lineal, 3 metres high |  |  |  |  |  |  |  |  |
|  |  | 2 metres buried, 2:1 batters | 13750 |  |  |  |  |  |  |  |
|  |  | Added September 2000 | 1500 |  |  |  |  |  |  |  |
|  |  | Added September 2002 | 1000 |  |  |  |  |  |  |  |
|  |  | Added April 2003 | 500 |  |  |  |  |  |  |  |
|  |  | Added March 2004 | 510 |  | 30 |  |  |  |  |  |
| 9 |  | Rockwork |  |  |  |  |  |  |  |  |
|  |  | 30 metres lineal, 3 metres high |  |  |  |  |  |  |  |  |
|  |  | 2 metres buried, 2:1 batters | 500 |  |  |  |  |  |  |  |
|  |  | Added March 2011-MBD | 1125 |  |  |  |  |  |  |  |
| 10 |  | Rock retard |  |  |  |  |  |  |  |  |
|  |  | 50 metres lineal |  |  |  |  |  |  |  |  |
|  |  | 6 metres bottom width |  |  |  |  |  |  |  |  |
|  |  | 2 metres top width |  |  |  |  |  |  |  |  |
|  |  | 3 metres high |  |  |  |  |  |  |  |  |
|  |  | 2 metres deep |  |  |  |  |  |  |  |  |
|  |  | 2:1 batters | 2000 |  |  |  |  |  |  |  |
| 11 |  | Rock retard |  |  |  |  |  |  |  |  |
|  |  | 15 metres lineal, 6 metre bottom width, |  |  |  |  |  |  |  |  |
|  |  | 2 metres high, 2 metres deep | 500 |  |  |  |  |  |  |  |
| 12 |  | Rock retard |  |  |  |  |  |  |  |  |
|  |  | 25 metres lineal, 6 metres bottom width, |  |  |  |  |  |  |  |  |
|  |  | 3 metres high, 2 metres deep | 800 |  |  |  |  |  |  |  |
| 13 |  | Rock retard (40 metres) |  |  |  |  |  |  |  |  |
|  |  | (a) 20 metres lineal, 3:1 batters |  |  |  |  |  |  |  |  |
|  |  | 3 metres vertical, 1.5m thick | 600 | 800 |  |  |  |  |  |  |
|  |  | (b) 20 metres lineal, 2:1 batters |  |  |  |  |  |  |  |  |
|  |  | 8 metre bottom width |  |  |  |  |  |  |  |  |
|  |  | 4 metre top width |  |  |  |  |  |  |  |  |
|  |  | 6 metres high (2m deep) | 1600 |  |  |  |  |  |  |  |
| 14 |  | Rock spur |  |  |  |  |  |  |  |  |
|  |  | 150 tonnes |  |  |  |  |  |  |  |  |
|  |  | 200 tonnes in boil hole |  |  |  |  |  |  |  |  |
|  |  | (constructed 4.8.93) | 350 |  |  |  |  |  |  |  |
| 15 |  | Rock retard |  |  |  |  |  |  |  |  |
|  |  | Cut off flood channel |  |  |  |  |  |  |  |  |
|  |  | (constructed 4.8.93) | 300 |  |  |  |  |  |  |  |
|  |  | added 1997/98 | 350 |  |  |  |  |  |  |  |
|  |  | added 1997/98 | 800 |  |  |  |  |  |  |  |
|  |  | taken 1997/98 | -150 |  |  |  |  |  |  |  |
|  |  | added december 99 | 40 |  |  |  |  |  |  |  |
|  |  | added december 99 | 1000 |  |  |  |  |  |  |  |
|  |  | added december 99 | 50 |  |  |  |  |  |  |  |
|  |  | Added September 2000 | 1200 |  | 40 |  |  |  |  |  |
|  |  | Added September 2002 | 460 |  |  |  |  |  |  |  |
|  |  | Added April 2003 | 790 |  |  |  |  |  |  |  |
| 16 |  | added august 98 | 200 |  |  |  |  |  |  |  |
|  |  | Added April 2002 | 50 |  |  |  |  |  |  |  |
| 16 | a | Added April 2002 | 50 |  |  |  |  |  |  |  |
| 17 |  | added august 98 | 200 |  |  |  |  |  |  |  |
| 18 |  | added august 98 | 200 |  |  |  |  |  |  |  |
| 19 |  | added august 98 | 200 |  |  |  |  |  |  |  |
| 19 | a | Added new spur - April 2002 | 50 |  |  |  |  |  |  |  |
| 19 | b | Added new spur - April 2002 | 50 |  |  |  |  |  |  |  |
| 20 |  | added august 98 |  |  |  |  |  |  |  |  |
|  |  | added october 98 - Destroyed September 2000 |  |  |  |  |  |  |  |  |
|  |  | Added March 2004 | 80 |  |  |  |  |  |  |  |
| 21 |  | added august 98 |  |  |  |  |  |  |  |  |
|  |  | added october 98 - Destroyed September 2000 |  |  |  |  |  |  |  |  |
| 20 | a | Riprap reformed from #20 & #21 | 700 |  |  |  |  |  |  |  |
|  |  | Added March 2007 (Contract R 2006 / 13) | 252 |  |  |  |  |  |  |  |
|  |  | Added February 2008 ex Stockpile # 50 | 100 |  |  |  |  |  |  |  |
| 22 |  | added august 98 | 200 |  |  |  |  |  |  |  |
|  |  | added october 98 | 50 |  |  |  |  |  |  |  |
| 23 |  | added august 98 | 150 |  |  |  |  |  |  |  |
| 23 | a | added october 98 | 250 |  |  |  |  |  |  |  |
|  |  | Recovered March 2007 (To stockpile # 48) | -150 |  |  |  |  |  |  |  |
|  |  | Balance destroyed | -100 |  |  |  |  |  |  |  |
| 24 |  | added august 98 | 100 |  |  |  |  |  |  |  |
|  |  | Added March 2004 | 30 |  |  |  |  |  |  |  |
| 25 |  | added august 98 | 150 |  |  |  |  |  |  |  |
| 25 | a | Rock spur |  |  |  |  |  |  |  |  |
|  |  | Added March 2004 | 220 |  | 40 |  |  |  |  |  |
| 26 |  | added august 98 | 30 |  |  |  |  |  |  |  |
| 27 |  | added august 98 | 30 |  |  |  |  |  |  |  |
| 28 |  | added august 98 | 30 |  |  |  |  |  |  |  |
| 29 |  | added august 98 | 30 |  |  |  |  |  |  |  |
|  |  | Added March 2004 | 210 |  | 30 |  |  |  |  |  |
| 30 |  | added august 98 | 30 |  |  |  |  |  |  |  |
| 31 |  | added august 98 | 30 |  |  |  |  |  |  |  |
| 32 |  | added august 98 | 40 |  |  |  |  |  |  |  |
| 34 |  | added october 99 | 50 |  |  |  |  |  |  |  |
| 34 | a | added october 99 | 50 |  |  |  |  |  |  |  |
| 35 |  | added october 99 | 50 |  |  |  |  |  |  |  |
| 36 |  | added october 99 | 50 |  |  |  |  |  |  |  |
| 37 |  | added october 99 | 50 |  |  |  |  |  |  |  |
| 38 |  | added october 99 | 50 |  |  |  |  |  |  |  |
| 39 |  | added october 99 | 250 |  |  |  |  |  |  |  |
|  |  | Added September 2000 | 500 |  |  |  |  |  |  |  |
|  |  | Added April 2002 | 250 |  |  |  |  |  |  |  |
|  |  | added october 99 |  |  |  |  |  |  |  |  |
|  |  | Added September 2002 | 600 |  |  |  |  |  |  |  |
|  |  | Added April 2003 | 700 |  |  |  |  |  |  |  |
| 40 |  | added december 99 |  | 450 |  |  |  |  |  |  |
| 41 |  | added december 99 | 500 |  |  |  |  |  |  |  |
|  |  | Added September 2000 | 40 |  |  |  |  |  |  |  |
|  |  | added may 99 | 240 |  |  |  |  |  |  |  |
| 42 |  | added may 99 | 140 |  |  |  |  |  |  |  |
|  |  | Isolated rock spur recovered March 2007 | -100 |  |  |  |  |  |  |  |
|  |  | Balance lost (Destroyed) | -40 |  |  |  |  |  |  |  |
| 43 |  | added may 99 | 140 |  |  |  |  |  |  |  |
|  |  | Isolated rock spur recovered March 2007 | -100 |  |  |  |  |  |  |  |
|  |  | Balance lost (Destroyed) | -40 |  |  |  |  |  |  |  |
| 44 |  | Rock Work | 220 |  |  |  |  |  |  |  |
| 45 |  | Rock spur |  |  |  |  |  |  |  |  |
|  |  | Added March 2004 | 190 |  |  |  |  |  |  |  |
|  |  | New riprap added May 2005 | 1,600 |  |  |  |  |  |  |  |
|  |  | Added March 2007 (ex #42 & #43) | 200 |  |  |  |  |  |  |  |
| 45 | a | Rubble Riprap Added May 2005 |  |  | 200 |  |  |  |  |  |
| 46 |  | Rock spur / Riprap |  |  |  |  |  |  |  |  |
|  |  | Added March 2004 | 200 |  | 10 |  |  |  |  |  |
|  |  | Added March 2007 (Contract R 2007 / 13) | 250 |  |  |  |  |  |  |  |
| 47 |  | Rock spur |  |  |  |  |  |  |  |  |
|  |  | Added March 2004 | 80 |  | 20 |  |  |  |  |  |
|  |  | Added March 2007 (Contract R 2006 / 13) | 350 |  |  |  |  |  |  |  |
| 48 |  | District Council Deflector - Topped up May 2007 | 540 |  |  |  |  |  |  |  |
| 49 |  | new spur added May 2007 | 100 |  |  |  |  |  |  |  |
| 50 |  | New Stockpile added May 2007 - Contract R2007/4 |  |  |  | 1000 |  |  |  |  |
|  |  | Deducted February 2008 - Added to #20a |  |  |  | -100 |  |  |  |  |
| 51 |  | New Spur Added February 2008 -Contract R2008/1 | 700 |  |  |  |  |  |  |  |
| 52 |  | New Spur Added February 2008 -Contract R2008/1 | 100 |  |  |  |  |  |  |  |
| 53 |  | New Riprap added June 2009 - Contract R2009/8 | 500 |  |  |  |  |  |  |  |
| 54 |  | New Culvert Added September 2009 - R 2009/7 |  |  |  |  |  |  |  |  |
|  |  | Twin 1200mm concrete pipes & Alloy Floodgates |  |  |  |  | 26400.00 |  |  | 10125.00 |
|  |  | 22 pipes, Rock & Rubble aprons | 220 |  | 320 |  |  |  |  |  |
| 55 |  | New Culvert Added September 2009 - R 2009/7 |  |  |  |  |  |  |  |  |
|  |  | 7 x 450mm concrete pipes & Alloy Floodgates |  |  |  |  | 1701.00 |  |  | 900.00 |
|  |  | 22 pipes, Rock & Rubble aprons |  |  | 20 |  |  |  |  |  |
| 56 |  | New Culvert Added September 2009 - R 2009/7 |  |  |  |  |  |  |  |  |
|  |  | 7 x 450mm concrete pipes & Alloy Floodgates |  |  |  |  | 1701.00 |  |  | 900.00 |
|  |  | 22 pipes, Rock & Rubble aprons @ 415m |  |  | 20 |  |  |  |  |  |
| 57 |  | New Culvert Added September 2009 - R 2009/7 |  |  |  |  |  |  |  |  |
|  |  | 2 x 500mm Farmboss pipes under farm race |  |  |  |  | 1700.00 |  |  |  |
|  |  | 22 pipes, Rock & Rubble aprons @ 415m |  |  |  |  |  |  |  |  |
| 58 |  | New rubble riprap added September 2009 |  |  |  |  |  |  |  |  |
|  |  | at junction with creek - R 2009/7 over 60 metres |  |  | 220 |  |  |  |  |  |
| 59 |  | New rock spur upstream of twin culverts - Nov 2009 | 1000 |  |  |  |  |  |  |  |
|  |  | Summary |  |  |  |  |  |  |  |  |
|  |  | Unit Costs | $66817.00 | $117225.00 | $1010.00 | $900.00 | $31502.00 | $1800.00 | $856.00 | $11925.00 |
|  |  | Calculated Costs | $22.00 | $7.50 | $22.00 | $21 | $1.00 | $20.00 | $25.00 | $1.00 |
|  |  |  | $1,469,974.00 | $879,187.50 | $22,220.00 | $18900.00 | $31502.00 | $36000.00 | $214000.00 | $11925.00 |
|  |  | Total estimated Assets as at 30 June 2014 | $2,491,108.50 |  |  |  |  |  |  |  |
|  |  | Add 10% Contingencies to cover Design etc | $249,110.85 |  |  |  |  |  |  |  |
|  |  | Add 2% for Resource Consent Costs | $54,804.39 |  |  |  |  |  |  |  |
|  |  | Total Including Contingencies | $2,795,023.74 |  |  |  |  |  |  |  |