THE WEST COAST REGIONAL COUNCIL

KONGAHU DEVELOPMENT

RATING DISTRICT

ASSET MANAGEMENT PLAN

October 2014

##### CONTENTS

EXECUTIVE SUMMARY	3

SECTION 1: INTRODUCTION	4

SECTION 2: SERVICE LEVELS	6

SECTION 3: FUNDING	8

SECTION 4: PERFORMANCE MEASURES:	9

APPENDIX I - DEFINITION OF TERMS:	10

APPENDIX II - EXPENDITURE SINCE 1985	11

APPENDIX III – ASSET REGISTER AND INFRASTRUCTURE MAPS	12

# EXECUTIVE SUMMARY

Under the Local Government Act 2002 Councils are required to develop ‘Asset Management Plans’ to demonstrate that they are managing the infrastructure for which they have responsibility. The purpose of this Asset Management Plan is to provide a statement as to how assets associated with the ‘Kongahu Rating District’ will be managed over their lifetime.

The plan lists the current scheme assets, which include:

- 21.388 kilometres of drainage channels

- 6.741 kilometres of creek channels

- various concrete culverts

- floodgates

The total replacement value of these assets is estimated at $600,530 (June 2014).

The Asset Management Plan indicates the level of service provided by the assets, the methods of monitoring the condition of the assets, and determines the annual maintenance needed to retain the service level.

The average annual maintenance of the Kongahu Drainage Scheme to 2014 has been $6,456.  This covers all works within the defined boundaries of the scheme.

The scheme assets will be maintained such that they continue to provide the level of service in perpetuity.  Because they are maintained in perpetuity the scheme assets will be not be depreciated resulting in no requirement to fund depreciation.

# SECTION 1: DESCRIPTION

1.1	PURPOSE OF ASSET MANAGEMENT PLAN

Asset Management Plans define the objectives and performance standards of river and drainage schemes for which the Regional Council has the maintenance responsibility and provide a basis upon which their effectiveness can be measured. This plan:

-	Identifies the service level for the Kongahu Drainage Scheme Rating District.

- Describes the methods used to maintain the service capacity of the assets.

- Complies with the regulatory requirements of the Local Government Act 2002

  - BACKGROUND

The Kongahu Swamp covered an area of 1000 hectares in the Karamea District. The swamp extended from the Little Wanganui River to the Otumahana Lagoon over a length of approximately 8 kilometres.

The first proposal to drain the swamp was prepared by the Public Works Department in 1938 but no major work was carried out at that time. At the request of the Karamea Federated Farmers the Westland Catchment Board agreed to carry out a survey and prepare a proposal to drain the Kongahu Swamp.

The proposal included the construction of a contour drain on the eastern side of the swamp to pick up all surface water draining from the hill catchment, while the proposed re-grading and realignment of Blackwater Creek and the construction of an outfall drain from Blackwater Creek along the western side of the swamp would provide an outlet for internal farm drains.

The proposal also included the construction of a new bridge over the contour drain and the replacement of the bridge over Blackwater Creek with a flood gated box culvert. The estimated cost of the scheme works was $86,000.

The Kongahu Swamp Drainage Scheme proposal was forwarded to the National Water and Soil Conservation Authority for approval in October 1973 and the Authority granted approval to proceed with the scheme in September 1974. The scheme classification was formally adopted by the Westland Catchment Board on 26th May 1975. A loan to finance the ratepayer’s share of the scheme was approved by the National Provident Fund in July 1975.

On the 14th November 1975 tenders were invited for the construction of 181,000 cubic metres of earthworks over a length of 24.6 kilometres. Ten tenders were received for the work the lowest being Delta Construction from Whangarei who were subsequently awarded the contract. Work commenced in August 1976 and in May 1978 the company went into liquidation.

Tenders to complete the scheme were invited in June 1978. Eleven tenders were received for the completion of the scheme works with the successful tenderer being R.H. Pearson from Westport who commenced work in October 1978 and completed the contract in April 1981.

The area included in the scheme is predominantly dairy farming. Part of the swamp has been set aside as a Wildlife Reserve and Whitebait Breeding area. The area of land within the confines of the scheme is 783 hectares.

1.3	DESCRIPTION OF ASSETS

The Rating District control works consist of all those works outlined in the accompanying infrastructural assets register that forms part of this asset management plan. The total replacement value of these works was $600,530 as at 30 June 2014

  - MAINTENANCE EXPENDITURE

Appendix II shows the expenditure since 1992. The average annual expenditure on maintenance and capital works since 1992 has been $6,456.

# SECTION 2: SERVICE LEVELS

  - GENERAL

There is no hydrological information held on the Kongahu area in respect to flood events or maximum flows that the scheme is intended to provide drainage for.

The rating district do not wish to have any drain flow analysis undertaken to quantify the actual level of drainage that the scheme currently provides. The scheme structures will be maintained to the dimensions that they were originally constructed.

2.2	OBJECTIVE

The objective of the Kongahu Rating District is to maintain existing creeks and drains included in the scheme to their original design specifications.

2.3	MAINTENANCE

The maintenance of the Kongahu Development Scheme can be broken into two areas: Creek Maintenance and Drainage Maintenance.

Creek Maintenance

Creek maintenance includes the excavation of creek bed build up, and the removal of vegetation from within and around waterways to allow the fast passage of flood flows to prevent overtopping of creek banks.

Drain Maintenance

Drains are required to be cleaned out on a regular basis to maintain their original design capacity as per the plan specifications as well as the repair of any damage to bank batters.

A major new issue as at 2014 is the invasion of the aquatic weed parrot’s feather into the scheme’s creeks and drains. This aggressive weed is now present throughout the area and can clog up the drains affecting efficient water flows. It has spread beyond the drains during major floods into upstream as well as downstream areas. Roundup will not kill this plant but Garlon does a better job. With NIWA advice, Council staff are trying to develop the optimal method of keeping on top of this pest plant.

    - Maintenance Issues

- Maintain invert levels of drains and creeks.

- Repair erosion including structural problems and water damage.

- Maintain access ways to enable future maintenance.

- Regular spraying to manage weed growth and keep water flowing.

Well established grass covered banks have been proven to be effective in resisting erosion. During normal use damage can be caused by grazing stock causing slumping and damage to the banks of drains and creeks.

Banks and creek beds can be damaged in the event of an earthquake by vertical or horizontal displacement.  This could result in the slumping and filling of drainage through liquefaction of the surrounding land.

2.3.2	Typical maintenance works undertaken

-	ensure creeks and drains are kept clear of weed and debris.

- ensure any slumping of natural banks are repaired by excavation.

- control of weeds and unsuitable vegetation on creek and drainage batters by spraying.

2.4	MAINTENANCE PROGRAMMES

An annual maintenance programme will be prepared each year in consultation with the Kongahu Rating District prior to adoption by the Council for inclusion in the Annual Plan or Long Term Plan.

In preparing the annual maintenance programme consideration will be given to:

-	an inspection to identify works requiring immediate repair.

-	works anticipated as being required given a ‘normal’ season.

-	flexibility to meet unbudgeted damages.

An annual report will be presented to the Kongahu Ratepayers outlining the condition of the scheme assets, maintenance works and expenditure required for the coming financial year.

2.5	CAPITAL WORKS

Capital works are defined as works which increase the service level of the scheme.  Such work would include increasing the design standard or the area covered by a scheme.

The aim of maintenance is to ensure the infrastructure assets are kept at a standard where they can always perform to their designed performance potential.

# SECTION 3: FUNDING

3.1	MAINTENANCE

Maintenance is funded by targeted rates, the level of rating being determined each year in the Annual Plan process. This involves:

(a)	Preparation of an annual works programme and corresponding budget in consultation with the Rating District Committee.

(b)	Adoption of works report and budget at rating District Annual Meeting.

(c)	Adoption of budget in Annual Plan by Council.

3.2	DAMAGE REPAIRS

Routine damage repairs are funded by a combination of:

-	carrying out work as scheduled in annual works programme.

-	reprioritising works identified in the annual works programme.

-	use of financial reserves.

Major damage repairs would be funded by loans raised by the Council and repaid by targeted rating over a number of years.

3.3	FINANCIAL RESERVES

Financial reserves are held within each rating districts account to provide the following:

-	meet the costs of unscheduled works.

-	enable an immediate response to flood damage repairs.

-	prevent major fluctuation in rating levels annually.

The level of financial reserves held in each rating account are determined by the assessment of risk damage and the need for unprogrammed works. The target prudent reserve for this rating scheme is $50,000.

3.4	DEPRECIATION

Drainage schemes are designed to be maintained in perpetuity by constantly repairing parts which are damaged by floods or by wear and tear encountered in a wet environment.

The performance measure is that the infrastructure assets are maintained to meet their service levels at all times.

As there is a constant cycle of replacement of elements of the infrastructure as necessary, depreciation of the value of the assets is not appropriate and funding of depreciation is not necessary. This approach is consistent with the NZ Infrastructure Asset Valuation and Depreciation Guidelines, Section 5.4.4.

# SECTION 4: PERFORMANCE MEASURES:

The overall performance measure is that the infrastructure assets are maintained to meet their service level at all times.

The following procedures will be adopted to measure the adequacy of maintenance.

Annually

- Produce annual works report to rating district annual meeting to include type of work to be undertaken, quantities, location and costs.

- Organise contracts for agreed scheme work, oversee contract completion and report to Council.

(iii)	Report on works undertaken during the previous financial period to the Rating District ratepayers and Council.

Performance Measure

No reports of channel and creek works requiring repairs without an agreed programme of remedial work in progress.

Triennially

(i)	Revaluation of the existing infrastructural assets.

- Review this Asset Management Plan

Performance Measure

Report to Council and Kongahu Ratepayers on revaluation of assets and review of this Plan.

# APPENDIX I - DEFINITION OF TERMS:

| DRAINAGE WORKS | Drainage works include rivers and drains presently managed to collect and convey stormwater safely away so that it does not backup or pond on the land surface. |
| --- | --- |
| FLOODPLAIN | The area of land adjacent to a river over which floodwater has historically or could potentially flow. The fan which has been built up in geological time by the river. |
| MAINTENANCE | Work required to keep the existing flood protection works in good repair, and includes spraying of stopbanks for weed control, topping up of earthwork for stopbanks and rock replacement. |
| RATEPAYERS | All individuals, or entities, whose property falls within the Rating District boundary and who pay a targeted rate towards the Scheme. |
| STOPBANK | Compacted earth structures generally parallel to the river channel designed to increase the depth of water and hence capacity without overflow. |

# APPENDIX II - EXPENDITURE SINCE 1992

| Works Expenditure |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 |
| 2,023 | 3,742 | 6,847 | 8,991 | 10,786 | 3,329 | 4,134 | 16,377 |
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 |  |
| 2,744 | 4,226 | 2,936 | 11,884 | 3,210 | 3,959 | 5,349 |  |
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 |
| 4,466 | 4,875 | 14,591 | 5,640 | 7,088 | 6,078 | 4,587 | 10,633 |
| Total Expenditure |  | $ 148,495 |  |  |  |  |
| Average Expenditure |  | $ 6,456 |  |  |  |  |
| Average Expenditure |  | 4.34% |  |  |  |  |
| as a % of Asset Value |  |  |  |  |  |

As at 30 June 2014, the value of the Kongahu Rating District Scheme assets was $600,530

APPENDIX III – ASSET REGISTER AND INFRASTRUCTURE MAPS

|  |  | KONGAHU RATING DISTRICT |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Infrastructural Assets - Amended to 30 June 2013 |  |  |  |  |  |  |  |
|  |  | Refer to drawing No. 951/32 Sheets 1-5 |  |  |  |  |  |  |  |
|  |  |  | Excavation | Excavation | Installation | Cleanout | Capital | Rock | Fill |
|  |  |  | Drain m³ | Channel m³ | dollar | dollar | dollar | tonne | m³ |
| 1 | a-b | Contour drain - 3970 lineal metres |  |  |  |  |  |  |  |
|  |  | 1.5 metes average bottom width |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters ($0.80/m3) | 17300 |  |  |  |  |  |  |
| 1 | b-c | Contour channel - 3200 lineal metres |  |  |  |  |  |  |  |
|  |  | 6.1 metres average bottom width |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters ($1.50/m3) |  | 44450 |  |  |  |  |  |
| 1 | c-d | Contour channel - 945 lineal metres |  |  |  |  |  |  |  |
|  |  | 9.1 metres average bottom width |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters ($1.50m3) |  | 19200 |  |  |  |  |  |
| 2 |  | Blackwater Creek - 1050 lineal metres |  |  |  |  |  |  |  |
|  |  | 4.5 metres average bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters ($1.5/m3) |  | 14000 |  |  |  |  |  |
| 3 |  | Deans Creek - 300 lineal metres |  |  |  |  |  |  |  |
|  |  | 1.5 metres bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters ($0.80/m3) | 1000 |  |  |  |  |  |  |
| 4 |  | 900 mm Concrete culvert |  |  |  |  |  |  |  |
|  |  | (June 1993 Valuation $1350) |  |  | $ 2,700.00 |  |  |  |  |
| 5 | a-b | Blackwater Drain |  |  |  |  |  |  |  |
|  |  | 2233 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters ($0.80/m3) | 13000 |  |  |  |  |  |  |
| 5 | b-c | Blackwater Drain |  |  |  |  |  |  |  |
|  |  | 1430 lineal metres |  |  |  |  |  |  |  |
|  |  | 1.5 metres bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters |  |  |  |  |  |  |  |
|  |  | ($0.80/m3) | 8500 |  |  |  |  |  |  |
| 5 | c-d | Blackwater Creek |  |  |  |  |  |  |  |
|  |  | 1348 lineal metres |  |  |  |  |  |  |  |
|  |  | 6.1 metres bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters ($1.50/m3) |  | 10190 |  |  |  |  |  |
| 5 | d-e | Blackwater Creek |  |  |  |  |  |  |  |
|  |  | 3742 lineal metres |  |  |  |  |  |  |  |
|  |  | 7.6 metres bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters ($1.50/m3) |  | 12652 |  |  |  |  |  |
| 5 | e-f | Blackwater Creek |  |  |  |  |  |  |  |
|  |  | 301 lineal metres |  |  |  |  |  |  |  |
|  |  | 9.1 metres bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters |  |  |  | $ 3,000.00 |  |  |  |
| 6 | a | 2 x 1200mm diameter fibreglass |  |  |  |  |  |  |  |
|  |  | floodgates (June 1993 Valuation $25,000 |  |  |  |  | $ 35,000.00 |  |  |
| 6 | b | 2 Wooden floodgates |  |  |  |  |  |  |  |
|  |  | (June 1993 Valuation $15,000) |  |  |  |  | $ 25,000.00 |  |  |
| 6 | c | added since 30/6/98 |  |  |  |  |  | 60 |  |
| 7 |  | 900mm Concrete culvert |  |  |  |  |  |  |  |
|  |  | (June 1993 Valuation $1350) |  |  | $ 2,700.00 |  |  |  |  |
| 8 |  | Drain 5-700 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters average |  |  |  |  |  |  |  |
|  |  | Depth 1.7 metres ($0.80/m3) | 4560 |  |  |  |  |  |  |
| 9 |  | Drain 8 - 600 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters average |  |  |  |  |  |  |  |
|  |  | Depth 1.7 metres ($0.80/m3) | 3910 |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |  |  |  |
|  |  | Drain 2 - 4500 lineal metres |  |  |  |  |  |  |  |
|  |  | 1.5 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters average |  |  |  |  |  |  |  |
|  |  | Depth 1.8 metres (0.80/m3) | 45630 |  |  |  |  |  |  |
| 11 |  | 1200 mm concrete culvert |  |  |  |  |  |  |  |
|  |  | (June 1993 Valuation $2000) |  |  | $ 4,000.00 |  |  |  |  |
| 12 |  | 1200 mm concrete culvert |  |  |  |  |  |  |  |
|  |  | (June 1993 Valuation $2000) |  |  | $ 4,000.00 |  |  |  |  |
| 13 |  | Drain 4 - 570 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters average depth |  |  |  |  |  |  |  |
|  |  | 1.6 metres (0.80/m3) | 3350 |  |  |  |  |  |  |
| 14 |  | 1000m concrete culvert |  |  |  |  |  |  |  |
|  |  | (June 1993 Valuation $2000) |  |  | $ 4,000.00 |  |  |  |  |
| 15 |  | Drain 7 - 540 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters average depth |  |  |  |  |  |  |  |
|  |  | 1.6 metres (0.80/m3) | 3170 |  |  |  |  |  |  |
| 16 |  | Drain 6-600 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters |  |  |  |  |  |  |  |
|  |  | Average depth 1.6 metres ($0.80/m3) | 3525 |  |  |  |  |  |  |
| 17 |  | 1200mm Concrete culvert |  |  |  |  |  |  |  |
|  |  | (June 1993 Valuation $2000) |  |  | $ 4,000.00 |  |  |  |  |
| 18 |  | 900mm Concrete culvert |  |  |  |  |  |  |  |
|  |  | (June 1993 Valution $1350) |  |  | $ 2,700.00 |  |  |  |  |
| 19 |  |  |  |  |  |  |  |  |  |
|  |  | Drain 3 - 600 lineal metres |  |  |  |  |  |  |  |
|  |  | 1.5 bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters |  |  |  |  |  |  |  |
|  |  | Average depth 1.7 metres |  |  |  |  |  |  |  |
|  |  | ($0.80/m3) | 4420 |  |  |  |  |  |  |
| 20 |  | Drain 1 - 700 lineal metres |  |  |  |  |  |  |  |
|  |  | 1.5 metres bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters |  |  |  |  |  |  |  |
|  |  | Average depth 1.7 metres ($0.80/m3) | 5160 |  |  |  |  |  |  |
| 20 | a | Drain 1 -300 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters |  |  |  |  |  |  |  |
|  |  | Average depth 1.7 metres ($0.80/m3) | 1955 |  |  |  |  |  |  |
| 21 |  | Rock rip rap - 40 metres |  |  |  |  |  |  |  |
|  |  | (400 tonnes at $15/tonne) |  |  |  |  |  | 400 |  |
| 21 | a | Stopbank - 40 lineal metres |  |  |  |  |  |  |  |
|  |  | Average height 2m, 3m topwidth |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters |  |  |  |  |  |  | 500 |
| 22 |  | Drain 500 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bottom width |  |  |  |  |  |  |  |
|  |  | 1.5 : 1 batters |  |  |  |  |  |  |  |
|  |  | Average depth 1.7 metres ($0.80/m3) | 3255 |  |  |  |  |  |  |
|  |  | Summary | 118735 | 100492 | $ 24,100.00 | $ 3,000.00 | $ 60,000.00 | 460 | 500 |
|  |  | Unit Rates | $1.50 | $ 2.50 |  |  |  | $ 30.00 | $ 10.00 |
|  |  | Calculated amounts | $178,102.50 | $251,230.00 | $ 24,100.00 | $ 3,000.00 | $ 60,000.00 | $ 13,800.00 | $ 5,000.00 |
|  |  | Total estimated assets as at 30 June 2013 | $535,232.50 |  |  |  |  |  |  |
|  |  | Add 10% Contingencies to cover Design etc | 53,523.25 |  |  |  |  |  |  |
|  |  | Add 2% for Resource Consent Costs | 11,775.12 |  |  |  |  |  |  |
|  |  | Total Including Contingencies | $600,530.87 |  |  |  |  |  |  |